## Slide 1: Power Plant Technology Fuel and Combustion (Lecture 1)
by
Mohamad Firdaus Basrawi, Dr. (Eng) Mechanical Engineering Faculty mfirdausb@ump.edu.my

## Slide 2
FUEL AND COMBUSTION
A Primary fuels in boiler are the fossil fuels in the form of coal, oil and gas.
Waste heat from Industrial wastes (coke oven gas, blast furnace gas, refinery gas,etc.), and waste biomass (sugar factory refuse [bagasse], sow mill wood dust, rise husk, etc.) can be used as fuels.
Combination firing: More then one type of fuel is simultaneously burned.
Coal
http://www.green-planet-solar-energy.com/forming-fossil-fuels.html
Vegetable matter which grew from millions of year ago under anaerobic environment.

## Slide 3
Peat
Lignite
Sub bituminous
Bituminous
Anthracite
Fixed C: 86 - 97% and less volatile matter
Fixed C: 46-86% and Volatile matter: 20-40%
Lowest grade of coal containing 25 - 35% carbon and high volatile matter
The first geological step to form coal. Contains 90 percent moisture)
Coal types:
35 – 45 % carbon
https://commons.wikimedia.org/wiki/File:Schultz_Sphagnum_Peat_Moss.jpg
https://commons.wikimedia.org/wiki/File:Pliocene_Lignite_Coal_Serbia.jpg
https://commons.wikimedia.org/wiki/File:Bituminous_Coal.JPG
https://commons.wikimedia.org/wiki/File:Ibbenbueren_Anthracite.JPG

## Slide 4
Coal Analysis
Quality of coal is important to determine its usufullness.
There are two types of coal analysis based on chemical composition:
Proximate: The "proximate" analysis coal using pyrolysis (950oC), the fixed carbon and the ash remaining after combustion. Proximate analysis is the most often used analysis for characterizing coals.
Ultimate: The "ultimate” analysis has composition of the biomass in wt%.

## Slide 5
No | Objective: To measure content of | Sample weigh (g) | Process |  |  | Result
 |  |  | Temperature (OC) | Periods (minutes) | methods | 
1 | The moisture | 1 | 105 | 60 | heated | M
2 | The moisture and volatile Matter | 1 | 950 | 7 | Placed in a covered platinum crucible and heated | VM
3 | The carbon | 1 | 720 | Until constant weight reached | Uncovered crucible completely burned | FC
Proximate analysis |  | FC+VM+M+A= |  |  |  | 100%
Proximate Analysis for Coal
FC+VM+M+A=100%
FC (Fixed Carbon), A (Ash), M (Moisture), VM (Volatile Matter)
There is a standard test methods ASTM D-7582-12.
(1)

## Slide 6
Coal rank compared with proximate analysis

## Slide 7
Ultimate Analysis
The ultimate analysis: chemical elements that comprise the coal substance, together with ash and moisture (100 percent of contents by mass).
There are standard test methods ASTM D-3178 (C & H), ASTM D-3179 (N), ASTM D-3177;ISO 334; ISO 351 (S), ASTM D-3173 (Moisture), ASTM D-3174 (Ash).
The analysis shows components below:
Carbon (C), Hydrogen (H), Oxygen (O), Nitrogen (N), Sulphur (S), moisture (M), and ash (A).
Therefore:
C+H+O+N+S+M+A=100% by mass
The dry and ash free analysis on combustible basis is obtained on dividing C, H, O,N and S by the fraction
(2)

## Slide 8
Two different heating values are cited for coal.
The higher heating value (HHV) considers the latent heat of vaporization of the water vapour formed by combustion (consider latent heat of water).
The lower heating value (LHV) considers that the water vapour formed by combustion leaves as vapour it self (not consider latent heat of water).
Therefore:
Where mw is water vapour formed in mass:
Where M and H are the mass fractions of moisture and hydrogen in the coal,
is the specific humidity of atmospheric air and wA is the actual amount of air supplied per kg of coal.
hfg is latent heat of vaporization 2.395 MJ/kg
*For energy balance and efficiency calculations of steam generators, HHV of fuel is considered in USA, whereas LHV is the standard used in European practice.
(3)
(4)

## Slide 9
HV can be experimentally determined using Calorimeters (generally a bomb calorimeter), but it can be estimated using equation.
The HHV of anthracite and bituminous coals can be approximated by using DULONG and PETIT formula:
Where C, H, O and S are mass fractions of carbon, oxygen, hydrogen, and sulphur in coal.
Assuming the latent heat of vaporization hfg of water vapour in the combustion products is equal to 2.395 MJ/kg, the lower heating value of coal is as below:
(6)
Where:
From Eq. (4)
(5)

## Slide 10
1 Btu/lbm =0.002326 MJ/kg
Exercise: Calculate the HHV by using DULONG & PETIT formula and compare with the given HHV.
Table 1: Proximate and ultimate analysis of some US coals
Analysis, mass percent
Anthracite
Bituminous
Subbituminous
Lignite
Proximate
Fixed carbon
Volatile matter
Moisture
Ash
Ultimate
C
H2
S
O2
N2
H2O
83.8
5.7
2.5
8.0
83.9
2.9
0.7
0.7
1.3
2.5
70.0
20.5
3.3
6.2
80.7
4.5
1.8
2.4
1.1
3.3
45.9
30.5
19.6
4.0
58.8
3.8
0.3
12.2
1.3
19.6
30.8
28.2
34.8
6.2
42.4
2.8
0.7
12.4
0.7
34.8

## Slide 11
Coal Property (Spontaneous Combustion & Autoignition
temperature)
Autoignition temperature
The autoignition temperature is the temperature that spontaneous ignition in normal atmosphere occured without external heat source.
This temperature is needed as the activation energy for combustion.
Cause and Ignition in Spontaneous Combustion
A substance including coal, hay, straw and peat that has a relatively low ignition temperature begins to release heat. This may occur by a little moisture and air, and bacterial fermentation also generates heat.
The heat is trapped (coal, hay, straw, peat, etc. are good thermal insulators), and the temperature of fuel increases, reaches ignition point.
Combustion begins if sufficient oxygen, and fuel are present.
Higher rank of the coal Lignite > bituminous >anthracite has low tendency to self ignite

## Slide 12
Coal Property (Spontaneous Combustion & Autoignition
temperature)
Flame temperature
Flame temperature is not simple because it depends on many factors including:
flow type (laminar, turbulent)
premixed or diffuse
Adiabatic or not
For flames in air, it also depends on the temperature, humidity, pressure, present gas mixture, etc. of the air
http://en.wikipedia.org/wiki/Autoignition_temperature
The temperature at which a chemical could ignite decreases when the pressure or oxygen concentration increases.
https://en.wikipedia.org/wiki/Adiabatic_flame_temperature

## Slide 13
Single particle coal combustion
http://www.metts.com.au/lignite-new-dedicated-approach.html

## Slide 14
Simple model of fixed carbon particle combustion
http://fluid.wme.pwr.wroc.pl/~spalanie/dydaktyka/combustion_MiBM/BCS/COAL_COMBUSTION.PDF
chemical reactions of char combustion :

## Slide 15
Common combustion (Pulverization of Coal)
Pulverization process is needed to produce pulverized coal or coal dust. This will increase the area for complete combustion.
Particle size is in the range of 75 microns, and each particle could have contact with the air. The energy loss due to unburned carbon is <0.5 %, and the boilers are very efficient.
http://www.climatetechwiki.org/technology/sup_crit_coal

## Slide 18
Slaging: A process of covering ofwalls (tubes) of furnace by mineral deposit, a result of combustion
Types:
Loose,
Bound (sintered, melted).

## Slide 20
FUEL OIL
Petroleum formed from decayed marine life, both vegetable and animal.
Oil accumulated in the rocks and sends below the earth’s crust.
http://www.green-planet-solar-energy.com/fossil-fuel-formation.html

## Slide 21
FUEL OIL
http://www.green-planet-solar-energy.com/fossil-fuel-formation.html
Petroleum formed from decayed marine life, both vegetable and animal.
Oil accumulated in the rocks and sends below the earth’s crust.

## Slide 22
FUEL OIL
Caprock
Natural gas
Oil
Water
An oil deposit
http://www.green-planet-solar-energy.com/fossil-fuel-formation.html
Petroleum formed from decayed marine life, both vegetable and animal.
Oil accumulated in the rocks and sends below the earth’s crust.

## Slide 23
Liquid fuels :
Easy to handle, store and burn
Almost constant heating value
Primarily a mixture of hydrocarbon that could also contain N2, O2 and S.
The hydrocarbons belong to the paraffin series (CnH2n+2) like:
Methane (CH4)
Ethane (C2H6)
Propane (C3H8)
Butane (C4H10)
Pentane (C5H12)
Hexane (C6H14)
Octane (C8H18)
(Gas form)
(Liquid form)
Hydrocarbon groups:
Isoparaffins
Cycloparaffins
Aromatic compounds

## Slide 24
Ultimate Analysis of oil indicates the mass fraction of C, H, O, N and S
Composition of hydrocarbon is fairly uniform within close with:
Carbon 83-87%, Hydrogen 11-16%, Oxygen + Nitrogen 0-7%, Sulphur 0-4%
Crude oil seldom used as distillation process into a number fractions such as:
The lighter fractions (lubrication oil, kerosene, light diesel oil, gasoline, aviation fuel, heavy diesel oil, etc)
The heavier fractions are used for boiler fuels and chemical production.
The physical properties requirement are:
pour point, flash point, Specific gravity, viscosity, and heating value.

## Slide 25
NATURAL AND PETROLEUM GAS
The transportation of natural gas is through pipeline.
Natural gas is the cleanest fossil fuels because it is free from ash and mixes well with air for complete combustion.
It consists of a mixture of the most volatile paraffins-methane to pentane, has a high hydrogen/carbon and therefore produces a lot of water when burned.
Liquid Natural Gas (LNG) is transported by tankers stored in spherical vessels.
Natural gas stored transported and stored as a super-cooled (cryogenic) liquid.
Compressed Natural Gas (CNG) is already used as fuel for automobile.
Liquid Petroleum Gas (LPG) refers to hydrocarbons (butane, propane, propylene, butylene) which are liquefied under moderate pressure and at normal temperatures. It is used as domestic fuel. It is by-product of petroleum refining

## Slide 26
Methane clathrate
http://en.wikipedia.org/wiki/Methane_clathrate
The worldwide amount of gas hydrates is estimated to twice the amount of fossil fuels on Earth

## Slide 27
Methane clathrate
http://www.mh21japan.gr.jp/english/mh21-1/3-2/
Since methane clathrates are stable at a higher temperature than LNG (−20 vs −162 °C), there is interest in storing natural gas into clathrates rather than liquifying it.
The production of natural gas hydrate (NGH) would require less refrigeration plant and energy.
However, the ice should also be transported and therefore it requires a ship of 7.5 times larger.

## Slide 28
SYNTHETIC FUELS
Synthetic fuels (synfuels) are gas and liquid fuels produced largely from coal in an economically and environmentally acceptable manner.
Coal Gasification
In the 19th century and the first part of the 20th century there was widespread use of coal gas for illuminating and and cooking purposes.
Coak is produced when coal is heated without oxygen until impurities such as H2, N2, O2 are removed.
The coke is burned with less air to yield the producer gas:
For each mole of oxygen in air there are 3.76 moles of nitrogen.
When the bed was heated to a high temperature, the air is replaced by steam and water gas is produced:
Old method
Coal gas obtained (CO+H2). The process is repeated until the coke exhausted.

## Slide 29
Modern method
Low heating value (synthesis gas, mixtures of water and producer gas)
Medium heating value ( producer mixed gas)
High heating value gas ( pipe line gas with properties close to that natural gas)
CO2+H2+CH4

## Slide 30
Coal gasification results in three gas mixtures and classified according to
their Heating value:
The feedstock is reacted with air and steam (The quality of air is less than stoichiometric)
CO2 from this reaction reacts further with addition carbon in the reach mixture:
In steam:
The result is low heating value syngas containing CO, H2, N2 and some CO2. It may also contain some CH4

## Slide 31
To obtain medium heating value gas, a shift reaction is used to produce
addition hydrogen, and nitrogen is removed
To produce pipe line gas, a catalytic methanation is carried out in which the products of water gas reacted over a nickel catalyst.
The product gas is high quality gas having a heating value of about 38 MJ/m3 and can directly substitute for natural gas.

## Slide 32
Hydrogasification is another advance method in which fluidized coal is gasified directly with hydrogen rich steam to methane-rich gas. The overall reaction is of the form:
Pretreater
vessel
400°C
7 MPa
Shift
converter
Cyclone
Separator
(cleaning)
Purifier
clean up
Nickel
catalyst
Dry crushed Coal
Steam
Steam
Oxygen
Oxygen
Coal
Synthesis
Gas
Gas
Dust and tar
Char and ash
Methanation
Pipe line gas (CH4) of high heating value
Synthane coal gasification process in US
To produce H2 and remove N2
Another advanced method
Gasifier
800°C
&
1000°C

## Slide 33
Underground Coal Gasification
Deposits of coal that could not be mined, might be economically utilized by underground gasification.
In situ coal gasification is attractive due to the following advantages:
It can extract energy from inaccessible reserves of coal that cannot be mined by conventional techniques.
When the mines become very deep, it be comes uneconomical to rise coal from such deep mines. In situ gasification can help raise energy from such abandoned mines.
It reduces mining personnel and equipment and needs less coal-handling and transportation facilities.
It is much safer and minimizes occupational hazards
Fuel gas produced by in situ gasification is cheaper than other energy forms.
When coal seams are thin, a higher recovery of the coal is possible.

## Slide 34
Rock or soil
Rock or soil
Pyrolysis area
Reduction area
Combustion area
Air inlet
Synthesis gas of low heating value (CO, CO2, CH4, H2)
In-situ coal gasification
Coal seam
All gases is seperated

## Slide 35
A head of the combustion zone is a reduction zone where carbon monoxide is formed
From moisture in the coal, water gas reaction can take place
Coal Liquefaction
The growing shortage petroleum supplies and the rapidly increasing cost of the oil has received interest in producing a liquid fuel from coal.
Coal liquefaction technology was stimulated in both Germany and Japan by the world War II.
Japan produced aviation gasoline in a large plant in North Korea which converted coke made from coal into calcium carbide in electric furnaces, then to acetylene, acetaldehyde, butyraldehide, octanol, and finally octane.
The most important, German process was the Fischer-Tropsch process, which is still used commercially by the SASOL plant in South Africa.
The conversion of coal into liquid fuel requires the addition of hydrogen to the coal. Coal has a ratio of hydrogen-carbon atoms of only 0.8 to 1, while in petroleum this ratio is 1.75 to 1.
There are three basic modes that have been used to liquefy coal:
(1) hydrogenation, (2) catalytic conversion, and (3) hydropirolysis.