## Slide 1: Power Plant Technology Energy Conservation in Power Plants (Lecture 2)
by
Mohamad Firdaus Basrawi, Dr. (Eng) Mechanical Engineering Faculty mfirdausb@ump.edu.my

## Slide 2
Auxiliary equipment for CHP and CCHP
https://en.wikipedia.org/wiki/File:Absorption_vs_adsorption.svg
Absorption is the process in which a fluid is dissolved by a liquid or a solid (absorbent).
Adsorption is the process in which atoms, ions or molecules from a substance (it could be gas, liquid or dissolved solid) adhere to a surface of the adsorbent. Adsorption is a surface-based process where a film of adsorbate is created on the surface while absorption involves the entire volume of the absorbing substance.

## Slide 3
Auxiliary equipment for CHP and CCHP
Absorption and Adsorption chillers converting heat to cooling energy mainly by replacing compressor with absorption or adsorption process
Absorption or Adsorption
https://hr.wikipedia.org/wiki/Datoteka:Refrigeration.png

## Slide 4
Auxiliary equipment for CHP and CCHP
H2O
LiBr
LiBr+H2O
LiBr
H2O
Qcool.
(Space cooling)
Qh.s
(Low temperature Heat Source)
Pe
(Pump)
Absorption chiller

## Slide 5
Auxiliary equipment for CHP and CCHP
One bed Adsorption chiller (Intermittant)
Condenser
Expansion
Device
Evaporator
Qevp
Adsorber
Qads
Qcool.
(Space cooling)
Condenser
Expansion
Device
Evaporator
Qevp
Qcdn
Adsorber
Qcool.
(Space cooling)
Qh.s
(Low temperature Heat Source)
Qgen

## Slide 6
Auxiliary equipment for CHP and CCHP
Qcool.
(Space cooling)
Qh.s
(Low temperature Heat Source)
http://www.sciencedirect.com/science/article/pii/S014070070800234X
Two bed Adsorption chiller (Continuous)
Not found

## Slide 7
Qcool.
(Space cooling)
Pe
(Air Compressor)
Qh.r
(total heat removed)
Auxiliary equipment for CHP and CCHP
Air-Conditioner
Input
Output
Qcool.
(Space cooling)
Pe
(Air Compressor)
https://hr.wikipedia.org/wiki/Datoteka:Refrigeration.png

## Slide 8
Qcool.
(Space cooling)
Pe
(Air Compressor)
Qh.r
(total heat removed)
Auxiliary equipment for CHP and CCHP
Air-Conditioner
Qh.r
(total heat removed)
Ab/Adsorption Chiller
Qh.s
(Low temperature Heat Source)
Qcool.
(Space cooling)
Pe
(Pump)
Input
Output

## Slide 9
Auxiliary equipment for CHP and CCHP
Comparison of COP

## Slide 10
Auxiliary equipment for CHP and CCHP

## Slide 11
Auxiliary equipment for CHP and CCHP
Power Sources | Heat source temp.(oC) | Matching technology
Gas turbine | ̴540 | Triple-effect/double-effect absorption
Solid oxide fuel cell | ̴480 | Triple-effect/double-effect absorption
Micro-turbine | ̴320 | double-effect/single-effect absorption
Phosphoric acid fuel cell | ̴120 | double-effect/single-effect absorption, desiccant cooling
Stirling engine | ̴90 | single-effect absorption, adsorption or desiccant cooling
IC engine | ̴250-450 ̴80 | double-effect absorption Single-effect absorption, adsorption or desiccant cooling
PEM fuel cell | ̴60 | adsorption or desiccant cooling
Recoverable energy qualities with matching technologies

## Slide 12
Auxiliary equipment for CHP and CCHP

## Slide 13
Auxiliary equipment for CHP and CCHP

## Slide 14
Auxiliary equipment for CHP and CCHP

## Slide 15
Auxiliary equipment for CHP and CCHP

## Slide 16
Example 1
Compare overall efficiency of a gas engine-cogeneration system (GE-CGS) and a conventional gas turbine power plant if the power and heat demand of the conventional system are same with the GE-CGS.
Gas engine-cogeneration system
Net electical efficiency 35%
Heat recovery efficiency 45%
Gas Turbine
Net electrical efficiency 33%
Boiler efficiency 90%
Trans. & Distr. Efficiency 93%

## Slide 17
Example 2
Compare overall efficiency of a gas engine-trigeneration system (GE-TGS) with an absorption chiller and a conventional gas turbine power plant with an air-conditioner if the power and cooling demand of the conventional system are same with the GE-TGS.
Gas engine-trigeneration system with absorption chiller
Net electical efficiency 35%
Heat recovery efficiency 45%
Absorp. Chiller COP 0.9
Percentage of recovered heat utilized for heating 20%
Gas Turbine with air-conditioner
Net electrical efficiency 33%
Air-conditioner COP 3.0
Heater efficiency 90%
Trans. & Distr. Efficiency 93%

## Slide 18
CL 5A
Compare overall efficiency of a gas engine-trigeneration system (GE-TGS) with an absorption chiller and a conventional gas turbine power plant with an air-conditioner if the power and cooling demand of the conventional system are same with the GE-TGS.
Micro Gas Turbine-trigeneration system with double-effect absorption chiller
Net electical efficiency 31%
Heat recovery efficiency 45%
Absorp. Chiller COP 1.2
Percentage of recovered heat utilized for heating 35%
Combined Cycle Gas Turbine with heater and air-conditioner
Net electrical efficiency 43%
Air-conditioner COP 3.0
Trans. & Distr. Efficiency 93%
Heater efficiency 90%
*Hardcopy of a report must also be submitted

## Slide 19
Return on Investment (ROI):
Simple ROI = (Gains – Investment Costs) / Investment Costs
=($125,000-$100,000) / $100,000 = 0.25 or 25%
Payback Period (PB):
Simple PB= Investment Costs / Annual Saving
=$125,000 / $25,000 = 5 years
Investments with shorter PB have lower risk than those with longer payback periods.
The problem with looking at simple ROI and PB: They tells you nothing about time.
How long will it take for your business to see that 25% return on investment?
What are the gains once the investment has paid for itself? Payback period doesn’t calculate this information.
Simple economic analysis of Power Plant (Life Cycle Cost)

## Slide 20
Simple economic analysis of Power Plant (Life Cycle Cost)
Life Cycle Cost:
Net Present Value= Electricity sold- capital cost -fuel cost -O&M cost
Consider Time and Time Value of money.
How long is the life cycle?
Depreciation of Money to the time. (Investment based)
Net Present or Net Future.
Single Amount
Present Worth Factor=1/(1+i)n
Future Worth Factor= (1+i)n
Uniform Series (e.g)Annual amount)
Present Worth Factor=[(1+i)n-1]/[i(1+i)n]
Future Worth Factor= [(1+i)n-1]/i
i=depreciation rate
n=Life time

## Slide 21
Simple economic analysis of Power Plant (Life Cycle Cost)
Single Amount
Present Worth Factor=1/(1+i)n
Future Worth Factor= (1+i)n
Kamal want to invest his RM10,000 for 20 years and expect 8% per year. Calculate amount that will be available after 20 years.
=RM10,000*(1+0.08)20
=RM10,000*(4.6610)
=RM46,610
i=depreciation rate
n=Life time

## Slide 22
Simple economic analysis of Power Plant (Life Cycle Cost)
Uniform Series (e.g)Annual amount)
Present Worth Factor=[(1+i)n-1]/[i(1+i)n]
Future Worth Factor= [(1+i)n-1]/i
A power plant was built with a cost of 1,000,000 and it is expected to generate an income of RM150,000 yearly from electricity sold. If the power plant is expected to have a lifetime of 20years, depreciation rate of 5%. What is the Net Profit as the Present Value?
=Revenue of selling electricity – Installation Cost
=150,000*[(1+0.05)20-1]/[0.05(1+0.05)20] – 1,000,000
=150,000*[2.653-1]/[0.05*2.653] – 1,000,000
=150,000*1.653/0.133 – 1,000,000
=150,000*12.43 – 1,000,000
=RM1,864,500 – 1,000,000
=RM864,500

## Slide 23
Simple economic analysis of Power Plant (Life Cycle Cost)
Net Present Value= Electricity sold- capital cost -fuel cost -O&M cost
Electricity sold [$]= Total Power Generated [kWh]* Price or Tariff [$/kWh]
Present Worth Factor
Total Power Generated [kWh] = Power Capacity [kW]* Operation Time [h] *
Load Factor [-] * Availability [-]
Capital Cost [$]= Prime Mover Cost [$/kW] * Installed Capacity [kW]
Fuel Price [$/kWhfuel] = Biogas Price [$/m3] / Biogas Heating Value [MJ/ m3] * MJ to kWh conversion factor (3.6 MJ/1kWh) [-]
Fuel Used [kWhfuel]= Total Power Generated [kWh] /Power Generation Efficiency [-]
O&M Cost [$]= Total Power Generated [kWh] * Running Cost [$/kWh]
Present Worth Factor
Present Worth Factor
Fuel Cost [$]= Fuel Used [kWhfuel]* Fuel Price [$/kWhfuel]

## Slide 24
CL5B
Calculate life-time profit (Net Profit) for all distributed generation types under Feed-in Tariff scheme. Use dollar currency for the calculation. Important parameters are shown below;
Maximum capacity: 300kW Biogas price: 0.50 RM/m3
Biogas heating value: 21.5 MJ/m3 Interest rate: 3.5%
Period: 21 years
Max demand: 300 kW (Load factor of 1.0, all are sold to grid)
Average solar availability: 0.18 (PV can only generate 30% of its maximum capacity)
Currency: 1$ = RM3.10
*Assume that the distributed generation running non-stop for 21years.
Net Present Value= Electricity sold- capital cost-fuel cost- O&M cost
DG types | Capital cost [$/kW] | Power generation efficiency [-] | Operation & Maintenance Cost ($/kWh) | FIT electricity price (RM/kWh)
Biogas-fuelled Diesel Engine | 125 | 0.43 | 0.005 | 0.32
Biogas-fuelled Gas Engine | 250 | 0.42 | 0.007 | 0.32
Biogas-fuelled Micro Gas Turbine | 350 | 0.30 | 0.005 | 0.32
Biogas-fuelled Fuel Cell | 1900 | 0.54 | 0.005 | 0.32
Photovoltaic | 3000 |  | 0.001 | 1.23