## Slide 1: Power Plant Technology Energy Conservation in Power Plants (Lecture 1)
by
Mohamad Firdaus Basrawi, Dr. (Eng) Mechanical Engineering Faculty mfirdausb@ump.edu.my

## Slide 2
Example 1
Compare overall efficiency of a gas engine-cogeneration system (GE-CGS) and a conventional gas turbine power plant if the power and heat demand of the conventional system are same with the GE-CGS.
Gas engine-cogeneration system
Net electical efficiency 35%
Heat recovery efficiency 45%
Gas Turbine
Net electrical efficiency 33%
Boiler efficiency 90%
Trans. & Distr. Efficiency 93%

## Slide 3
Example 2
Compare overall efficiency of a gas engine-trigeneration system (GE-TGS) with an absorption chiller and a conventional gas turbine power plant with an air-conditioner if the power and cooling demand of the conventional system are same with the GE-TGS.
Gas engine-trigeneration system with absorption chiller
Net electical efficiency 35%
Heat recovery efficiency 45%
Absorp. Chiller COP 0.9
Percentage of recovered heat utilized for heating 20%
Gas Turbine with air-conditioner
Net electrical efficiency 33%
Air-conditioner COP 3.0
Heater efficiency 90%
Trans. & Distr. Efficiency 93%

## Slide 4
CL 5A
Compare overall efficiency of a gas engine-trigeneration system (GE-TGS) with an absorption chiller and a conventional gas turbine power plant with an air-conditioner if the power and cooling demand of the conventional system are same with the GE-TGS.
Micro Gas Turbine-trigeneration system with double-effect absorption chiller
Net electical efficiency 31%
Heat recovery efficiency 45%
Absorp. Chiller COP 1.2
Percentage of recovered heat utilized for heating 35%
Combined Cycle Gas Turbine with heater and air-conditioner
Net electrical efficiency 43%
Air-conditioner COP 3.0
Trans. & Distr. Efficiency 93%
Heater efficiency 90%
*Hardcopy of a report must also be submitted