## Slide 1: Engineering Surveying Introduction to Survey Engineering
Introduction To Survey Engineering, by Mohd Arif
By
Mohd Arif Sulaiman
Faculty of Civil Engineering & Earth Resources
mdarif@ump.edu

## Slide 2: Chapter Description
Expected Outcomes
Able to explain the definition & principle of surveying
Able to demonstrate and understand the units measurement
Able to read and understand the information shown on site plans.
References
Barry F. Kavanagh, "Surveying with Construction Application", 0-13-048215-3 Pearson, Prentice Halll, 2004.
Bannister, Raymond, Baker,"Surveying",0-582-30249-8, Prentice Hall 1998.
William Irvine, "Surveying for Construction", 4th Ed.,0-07-707998-1, McGraw-Hill,1998.

## Slide 3: Coordinate System
Is use to locate a features on the earth’s surface or a two dimensional representation on this surface such as a map.
Characteristic:
Include stability, the ability to show a points, lines and area, and the ability to measured length, size and shape.

## Slide 4
Category
Geographic coordinate system
Rectangular coordinate system
Non coordinate system

## Slide 5: Geographic coordinate system
GCS uses a three dimensional spherical surface to define location on earth
It is uses degree of latitude and longitude to describe a location on the earth’s surface and also a datum based on spheroid

## Slide 7: Rectangular Coordinate System
This Grid line is obtained by projecting the lines of latitude or longitude from our representation of the world as a globe onto a flat surface using a map projection.
The lines of latitude and longitude become grid lines on a flat map.

## Slide 8
Type of Projection
Cone
Cylindrical
Azimuthal
Oblique
Equatorial
Polar
Transverse
Oblique
Mercator
Tangent
Secant

## Slide 9: Two dimensional system which is refer to the two axis known as easting and northing. Also known as Cartesian or orthogonal co ordinate system. Origin may refer to -RSO – Peninsular Malaysia -Cassini – State in Malaysia

## Slide 10: Non Coordinate System
No coordinate system will be used to define the location.
It location will be identify by using
Address
Linear referencing and etc.

## Slide 11
Author Information Dr Idris bin Ali
Dr Cheng Hock Tian