## Slide 1: CHAPTER 3
Engineering Surveying Traversing Survey and Computation
Introduction To Survey Engineering, by Mohd Arif
By
Mohd Arif Sulaiman
Faculty of Civil Engineering & Earth Resources
mdarif@ump.edu

## Slide 2: Chapter Description
Expected Outcomes
Able to explain the terminology used in traversing
Able to understand the procedure in traverse survey
Able to calculate the co-ordinate and all related information using traverse data.
References
Barry F. Kavanagh, "Surveying with Construction Application", 0-13-048215-3 Pearson, Prentice Halll, 2004.
Bannister, Raymond, Baker,"Surveying",0-582-30249-8, Prentice Hall 1998.
William Irvine, "Surveying for Construction", 4th Ed.,0-07-707998-1, McGraw-Hill,1998.

## Slide 3: Introduction to theodolite and EDM
the theodolite is an instrument that is used to measure vertical and horizontal angles, with an accurate varying from 1 to 60 second of arc.
It was invented by Roemer, astronomer in 1690.
EDM is used to measure angles and distance.

## Slide 4
Classified
Transit theodolite
Non-transit theodolite
Obsolete nowadays

## Slide 5
Classification
Vernier
Direct reading
Optical scale
Optical micrometer
Opto-electronic

## Slide 6: Component of theodolite

## Slide 7: Vertical circle

## Slide 8: Traverse terminology
Transit
It is also called plunging or reversing. This is the operation of revolving the telescope through 180 in a vertical plane about its horizontal axis
Face right
When the vertical circle of the theodolite is on the right of the observer
Face left
When the vertical circle of the theodolite is on the left of the observer

## Slide 9
Swinging the telescope
Revolving the telescope in a horizontal plane about its vertical axis
Telescope normal
The telescope is said to be normal or direct when its vertical circle is to be left of the observer
Telescope inverted
The telescope is said to be inverted when its vertical circle is to be right of the observer

## Slide 10
Meridian
It is a fixed direction in which bearing of survey lines are expressed
Bearing
It is the horizontal angle between the reference meridian and the survey line

## Slide 11
Meridian
True meridian
Grid meridian
Magnetic meridian
Arbitrary meridian

## Slide 12: Whole Circle Bearing
Whole circle bearing is a angle which is measured from north to survey line in clockwise direction.
The range from 0o to 360o

## Slide 13
FIRST
QUAD
2ND
QUAD
3RD
QUAD
4TH
QUAD

## Slide 14: Quadrant Bearing
The quadrant bearing is a angle which is measured from North or south toward to east or west.
The angle can be measured clockwise or counterclockwise
Its always accompanied by the letters that describe the quadrant in which the line is located (NE, SE, SW and NW).
The range from 0o to 90o

## Slide 15
N---W
N---E
S---W
S---E
Letter at start and end defines the quadrant
Angular value measured from N-S line
Quadrant Bearings

## Slide 16: Backward and Forward
The direction AB is a forward whole circle bearing. The angle value is measured from meridian to line AB and in clockwise direction.
This direction BA is known as the back whole circle bearing ; in exactly the reverse direction. The angular value is the clockwise angle the north point to the line BA.

## Slide 17: Deflection Angle
The deflection angles are measured from prolongation of the back line to the forward line. The angles are measured either in anti-clockwise (L) or clockwise (R) direction ; the direction (L or R) must be shown along with the numerical value.
L
R
L

## Slide 18
Measurement of Angles
Horizontal and Vertical Angles
• Horizontal angle: the angle formed in a horizontal plane by two intersecting vertical planes
• Vertical angle / Zenith angle: the angle formed in a vertical plane by two intersecting horizontal planes

## Slide 19
Measurement of Angles

## Slide 20
Given a quadrant bearing is N32°45’30”W, compute the equivalent whole circle bearing.
NW
32°45’30”
Bearing
Azimuth
360° - 32°45’30”
= 327°14’30”
2. Given a whole circle bearing is 122°12’36”, compute the equivalent Quadrant bearing.
Azimuth
122°12’36”
Bearing
180° - 122°12’36”
= S 52°47’24” E

## Slide 21: Types of traverse
Open traverse
A frame work which is end at point of unknown co-ordinate
Closed traverse
A frame work which start and finish at point of known co-ordinate and its normally form in polygon.

## Slide 22
Author Information Dr Idris bin Ali
Dr Cheng Hock Tian