## Slide 1: CHAPTER 3
Engineering Surveying Traversing Survey and Computation
Introduction To Survey Engineering, by Mohd Arif
By
Mohd Arif Sulaiman
Faculty of Civil Engineering & Earth Resources
mdarif@ump.edu

## Slide 2: Chapter Description
Expected Outcomes
Able to explain the terminology used in traversing
Able to understand the procedure in traverse survey
Able to calculate the co-ordinate and all related information using traverse data.
References
Barry F. Kavanagh, "Surveying with Construction Application", 0-13-048215-3 Pearson, Prentice Halll, 2004.
Bannister, Raymond, Baker,"Surveying",0-582-30249-8, Prentice Hall 1998.
William Irvine, "Surveying for Construction", 4th Ed.,0-07-707998-1, McGraw-Hill,1998.

## Slide 3: Setting out the theodolite
Temporary Adjustment
Centering
Leveling
up
Focusing

## Slide 4: Centering
(1) Establish the tripod roughly over the survey station
(2) Examine and memories the position on the instrument in the box

## Slide 5
(3) Attach the theodolite to the tripod
(4) Using the footscrew to inline the line of sight through the optical plammet, centre the plummet exactly on the survey point

## Slide 6: Levelling
slide the legs in or out until the circular barble is exactly centre
although the tripod movement may be excessive, the plummet will still be on the survey point
instrument is approximate centred and level
precisely level the instrument using the plate bubble
unclmp and move the whole instrument over the tripod until the plummet crosshair is exactly over the survey point
Repeat these 2 steps until the instrument is exactly centred and levelled.

## Slide 7: Focusing

## Slide 8: Traversing procedure and booking system

## Slide 9
Instrument Station
Reflector Station
Reflector Station
Back station
Forward station

## Slide 10
Used prismatic compass, say bearing 2-1 is 311 26 30
In face left, target to stn 1 and set bearing reading of 311 26 30
Again in face left, target stn 3 and take the reading, say 205 20 20
Transit theodolite from face left to face right. Then target to stn 1 and record the reading, say 140 10 20
Then target to stn 3 and record the reading, say 25 20 20
Now measure the horizontal distance. In face left measure the distance for twice.
FL 320 10 20
FR 140 10 20
FL 205 20 20
FR 25 20 20
Dist : 70.112,
70.112
Dist : 65.682,
65.680

## Slide 11
Booking System

## Slide 12
Instrument Station
Reflector Station
Reflector Station
Back station
Forward station

## Slide 13
4
2
3
Bearing Measurement
In face left, target to stn 2 and set bearing reading of 25 20 20
Again in face left, target stn 4 and take the reading, say 269 30 00
Transit theodolite from face left to face right. Then target to stn 2 and record the reading, say 205 20 20
Then target to stn 4 and record the reading, say 89 30 20
Distance Measurement
In face left, target to stn 4 then record the distance for twice. Say 1st reading is 57.667 and 2nd reading is 57.667

## Slide 14
Booking System

## Slide 15
Back station
Forward station
Bearing Measurement
In face left, target to stn 3 and set bearing reading of 89 30 20
Again in face left, target stn 5 and take the reading, say 340 39 40
Transit theodolite from face left to face right. Then target to stn 3 and record the reading, say 269 30 20
Then target to stn 4 and record the reading, say 160 39 40
Distance Measurement
In face left, target to stn 5 then record the distance for twice. Say 1st reading is 53.832 and 2nd reading is 53.834

## Slide 16
Back station
Forward station
Bearing Measurement
In face left, target to stn 3 and set bearing reading of 89 30 20
Again in face left, target stn 5 and take the reading, say 340 39 40
Transit theodolite from face left to face right. Then target to stn 3 and record the reading, say 269 30 20
Then target to stn 4 and record the reading, say 160 39 40
Distance Measurement
In face left, target to stn 5 then record the distance for twice. Say 1st reading is 53.832 and 2nd reading is 53.834

## Slide 20
Author Information Dr Idris bin Ali
Dr Cheng Hock Tian