## Slide 1: CHAPTER 3
Engineering Surveying Traversing Survey and Computation
Introduction To Survey Engineering, by Mohd Arif
By
Mohd Arif Sulaiman
Faculty of Civil Engineering & Earth Resources
mdarif@ump.edu

## Slide 2: Chapter Description
Expected Outcomes
Able to explain the terminology used in traversing
Able to understand the procedure in traverse survey
Able to calculate the co-ordinate and all related information using traverse data.
References
Barry F. Kavanagh, "Surveying with Construction Application", 0-13-048215-3 Pearson, Prentice Halll, 2004.
Bannister, Raymond, Baker,"Surveying",0-582-30249-8, Prentice Hall 1998.
William Irvine, "Surveying for Construction", 4th Ed.,0-07-707998-1, McGraw-Hill,1998.

## Slide 3: Balancing a traverse
It is clear that the closing error should be so distributed throughout the traverse that its effect is as little apparent on the plan as possible.
A traverse is balanced by applying correction to latitudes and departures. This is called balancing a traverse. This can be accomplished mathematically, i.e. by applying some rules, or graphically. There are two mathematical rules, which are as follows:

## Slide 4
Bowditch rule
It is also called compass rule. It is used to balance a traverse when the linear and angular measurements are equally precise. It is assumed that the errors in the linear measurements are proportional to √L, where L is the length of the line, and those in the angular measurements are inversely proportional to √L, which questionable. If equal weights are assigned to linear and angular measurements, the errors and hence the corrections are proportional to the lengths of the lines.
Correction to latitude (or departure of any side)
Transit rule
This method of adjusting the consecutive coordinates of traverse is purely empirical and there is no sound theoretical foundation for it. It is employed when the angular measurements are more precise as compared to the linear measurements (theodolite traversing).
Correction to latitude (of departure of any side)
Refer page 52
Refer page 52

## Slide 5
ERROR OF CLOSURE
PRECISION

## Slide 7
Linear misclosure = 1: 11950

## Slide 9
Line | Bearing | Length | Depart ΔE | Latitude ΔN | ΔE Correction | ΔN Correction | Corrected ΔE | Corrected ΔN | Easting | Northing | Stn
2 |  |  |  |  |  |  |  |  | 101.100 | -10.200 | 2
3 | 85 25 20 | 175.121 | 174.562 | 13.977 | 0.003 | 0.002 | 174.565 | 13.979 | 275.665 | 3.779 | 3
4 | 26 01 30 | 150.702 | 66.122 | 135.421 | 0.003 | 0.002 | 66.125 | 135.423 | 341.790 | 139.202 | 4
5 | 70 41 20 | 180.701 | 170.534 | 59.757 | 0.004 | 0.002 | 170.538 | 59.759 | 512.328 | 198.961 | 5
6 | 355 26 50 | 75.102 | -5.961 | 74.865 | 0.001 | 0.000 | -5.960 | 74.865 | 506.368 | 273.826 | 6
 | Sum | 581.626 | 405.257 -405.268 | 284.020 -284.026 |  |  | 405.268 | 284.026 | 405.268 | 284.026 | 
 | Error |  | -0.011 | -0.006 |  |  |  |  |  |  | 
 | Correction |  | 0.011 | 0.006 | 0.011 | 0.006 |  |  |  |  | 
 | Linear Mis-close |  | 1: 46419 |  |  |  |  |  |  |  | 

## Slide 10
Author Information Dr Idris bin Ali
Dr Cheng Hock Tian