## Slide 1: Engineering Surveying Introduction to Survey Engineering
Introduction To Survey Engineering, by Mohd Arif
By
Mohd Arif Sulaiman
Faculty of Civil Engineering & Earth Resources
mdarif@ump.edu

## Slide 2: Exercise #5
QUESTION 1
Figure Q1 shows the staff readings obtained from a survey a cross of a new road. Record the readings and calculate reduce levels and applying all the appropriate checks.
Figure Q1

## Slide 3
QUESTION 2
Table Q2 shows the results of a leveling along the centerline of the centre line of a proposed trench AB. The leveling commenced on TBM1 (10.000m Above MSL) and readings were taken at 5.000m intervals along the line.
a. Reduce the levels.
Determine the proposed trench, rising from the existing invert level (7.570m
Above MSL) of manhole A at a gradient of 1 in 75.
Given that the trench is to be 0.5m wide, calculate the volume of material to
be removed to form the excavation.

## Slide 4
BS | IS | FS | Rise | Fall | Surface RL | Grade RL | Fill | Cut | Remarks
0.850 |  |  |  |  | 10.000 |  |  |  | TBM1
 | 3.502 |  |  |  |  |  |  |  | A Ch00
 | 2.163 |  |  |  |  |  |  |  | Ch5
 | 1.296 |  |  |  |  |  |  |  | Ch10
 | 1.076 |  |  |  |  |  |  |  | Ch15
3.200 |  | 0.243 |  |  |  |  |  |  | Cp1
 | 2.782 |  |  |  |  |  |  |  | Ch20
 | 3.421 |  |  |  |  |  |  |  | Ch25
 | 2.357 |  |  |  |  |  |  |  | Ch30
1.720 |  | 0.682 |  |  |  |  |  |  | Cp2/Ch35
 | 2.783 |  |  |  |  |  |  |  | Ch40
 | 1.716 |  |  |  |  |  |  |  | Ch45
 | 1.026 |  |  |  |  |  |  |  | B Ch50
 |  | 1.000 |  |  | 13.845 |  |  |  | TBM2
Figure Q1

## Slide 5
Author Information Dr Idris bin Ali
Dr Cheng Hock Tian