## Slide 1: Engineering Surveying Introduction to Survey Engineering
Introduction To Survey Engineering, by Mohd Arif
By
Mohd Arif Sulaiman
Faculty of Civil Engineering & Earth Resources
mdarif@ump.edu

## Slide 2: Quiz #1

## Slide 3
Question 1
From the drawing given, answer all the question below
ABCD – Boundary line of lot
CD – Sewerage line
LP – Lamp post
Given that the scale of drawing is 1:750,
a. Determined dimensions of building in unit m and building area in
unit m2,
b. Determined coordinates of lamp post,
c. Dalculate gradient of sewerage line EF.

## Slide 4
Question 2
Location of any point on earth surface was defined by coordinate value. Give a reason, why a point has difference coordinate value?
Question 3
List out FOUR (4) of the measurement techniques to locate features using in survey work.
Question 4
The principle of surveying is “From The Whole to The Part”. How does the principle employ in Linear Survey work?

## Slide 5
Question 5
A rectangular parcel of land has sides measuring 120 chain and 55 chain. What is the area of the property in square meters, square kilometers and acres?
i. ______________ square meters
ii. ______________ square kilometers
iii. ______________ acres
(Notes: 1 chain = 20.1168m ; 1 acres = 10 square chain)

## Slide 6
Author Information Dr Idris bin Ali
Dr Cheng Hock Tian