## Slide 1: Digital Electronics Number Systems and Codes
Prepared by: Norazian Subari
Fakulti Kejuruteraan Elektrik & Elektronik aziansubari@ump.edu.my
Credited to: Faradila Naim, Nurul Wahidah Arshad

## Slide 2: Chapter Description
Expected Outcomes
At the end of this topic, students should be able to:
  Convert a number from one system (decimal, binary, octal, hexadecimal) to its equivalent in one of the other number systems.
  Discuss the difference between BCD and binary numbers.
  Explain the purpose of alphanumeric codes such as the ASCII code.

## Slide 3: Topics
Decimal, Binary, Octal and Hexadecimal Number Systems.
Conversion between Number System
Numbering Code
Alphanumeric Code
Signed Number
  Signed and Magnitude
  1st and 2nd Compliment
  Addition and Subtraction

## Slide 4: DIGITAL number systems
Number Systems
Decimal
Binary
Octal
Hexadecimal

## Slide 5: DIGITAL number systems (Decimal)
Source: https://drstienecker.com

## Slide 6: DIGITAL number systems (binary)
Source: https://drstienecker.com

## Slide 7: DIGITAL number systems (octal)
Source: https://drstienecker.com

## Slide 8: DIGITAL number systems (hexadecimal)
Source: https://drstienecker.com

## Slide 9: Conversion between number systems
Decimal Conversion
Binary
Octal
Binary Conversion
Decimal
Octal
Octal Conversion
Decimal
Binary
Hexadecimal
Hexadecimal
Hexadecimal Conversion
Decimal
Binary

## Slide 10: Decimal conversion: decimal to binary
MSB
LSB
MSB – Most Significant Digit
LSB – Least Significant Digit
Divide the decimal number by 2 until the quotient is 0.

## Slide 11: Decimal conversion: decimal to octal
MSB
LSB
MSB – Most Significant Digit
LSB – Least Significant Digit
Divide the decimal number by 8 until the quotient is 0.

## Slide 12: Decimal conversion: decimal to hexadecimal
MSB
LSB
MSB – Most Significant Digit
LSB – Least Significant Digit
Divide the decimal number by 16 until the quotient is 0.

## Slide 13: binary conversion: binary to decimal
(11101) 2 = (1x23) + (1x23) + (1x22) + (1x01 ) + (1x20)
= 16 + 8 + 4 + 1
= (29)10
Multiply each binary number by its weight and summing the products

## Slide 14: binary conversion: binary to octal
Grouped of three bits starting at the LSB
Then convert each group to its octal equivalent

## Slide 15: binary conversion: binary to hexadecimal
Grouped of four bits starting at the LSB
Then convert each group to its octal equivalent
Zeros are added to make each group complete with 4 bits

## Slide 16: octal conversion: octal to decimal
(362) 8 = (3x82) + (3x81) + (3x80)
= 192 + 48 + 2
= (242)10
Multiply each octal number by its weight and summing the products

## Slide 17: octal conversion: octal to binary
Convert each octal digit to its three-bit binary equivalent.

## Slide 18: hexadecimal conversion: hexadecimal to decimal
Multiply each hexadecimal number by its weight and summing the products
(19B) 16 = (1x162) + (9x161) + (11x160)
= 256 + 144 + 11
= (411)10

## Slide 19: hexadecimal conversion: hexadecimal to binary
Convert each hexadecimal digit to its four-bit binary equivalent.

## Slide 20: Arithmetic operations of the number systems
Binary Addition & Subtraction
Octal Addition & Subtraction
Hexadecimal Addition & Subtraction

## Slide 21: Arithmetic operations of the number systems
Binary
Additional
0 + 0 = 0 Sum of 0 with a carry of 0
Subtraction
Additional
0 - 0 = 0
0 + 1 = 1 Sum of 1 with a carry of 0
1 + 0 = 1 Sum of 1 with a carry of 0
1 + 1 = 10 Sum of 0 with a carry of 1
1 - 1 = 0
1 - 0 = 1
10 - 1 = 1 0 - 1 with a borrow of 1

## Slide 22: Arithmetic operations of the number systems
Octal
Additional
0 + 0 = 0 Sum of 0 with a carry of 0
Octal
Additional
0 - 0 = 0
0 + 1 = 1 Sum of 1 with a carry of 0
1 + 0 = 1 Sum of 1 with a carry of 0
1 + 1 = 10 Sum of 0 with a carry of 1
1 - 1 = 0
1 - 0 = 1
10 - 1 = 1 0 - 1 with a borrow of 1

## Slide 23: Arithmetic operations of the number systems
Hexadecimal
Additional
0 + 0 = 0 Sum of 0 with a carry of 0
Hexadeciaml
Additional
0 - 0 = 0
0 + 1 = 1 Sum of 1 with a carry of 0
1 + 0 = 1 Sum of 1 with a carry of 0
1 + 1 = 10 Sum of 0 with a carry of 1
1 - 1 = 0
1 - 0 = 1
10 - 1 = 1 0 - 1 with a borrow of 1

## Slide 24: Numbering code
* Codes : A special group of symbols
* Encode : Representing number letter or words into a code
Numbering Code
Gray Code
BCD Code

## Slide 25: Numbering code (BCD CODE)
BCD CODE
Coding decimal to its binary equivalent
Code available
0000 - 1001
Four bits = one decimal digit

## Slide 26: Numbering code (gray CODE)
Binary to Gray Code
Gray to Binary Code

## Slide 27: Alphanumeric code
See the entire table in textbook.

## Slide 28: Signed number
Changing each of the bit value.
01
10
The remaining bits are the magnitude bits.
Eg: Express -25 in an 8-bit sign-magnitude binary number.
2510 = 00011001
-2510 = 10011001

## Slide 29: 1’s Complement
Changing each of the bit value.
01
10
+ve no.: same as +ve sign-magnitude.
-ve no.: the 1’s complement of the corresponding +ve number.

## Slide 30: 2’s Complement
+ve no.: same as +ve sign-magnitude.
-ve no.: 2’s complement of the corresponding +ve number.
Obtained by adding 1 to the 1’s complement of the corresponding number.

## Slide 31: References
  T. Floyd, “Digital Fundamental”, 10th Ed., USA : Prentice-Hall, 2008.
  R.J. Tocci, “Digital Systems: Principles and Applications”, 10th Ed., USA : Prentice-Hall, 2006.

## Slide 32: Norazian Subari Fakulti Kejuruteraan Elektrik & Elektronik Universiti Malaysia Pahang 26600 Pekan, Pahang, Malaysia http://fkee.ump.edu.my/index.php/en/staff-menu/articles-staff/1622-norazian-subari-main-profile