## Slide 1: Digital Electronics Logic Gates and Boolean Algebra
by
Norazian Subari
Fakulti Kejuruteraan Elektrik & Elektronik aziansubari@ump.edu.my

## Slide 2: Chapter Description
Expected Outcomes
At the end of this topic, students should be able to:
  Perform the basic logic operations.
  Describe the operation and construct the truth tables for each logic circuit.
  Write the Boolean expression for the logic gates and their combinations.
  Use the Boolean algebra to simplify complex logic circuits.

## Slide 3: Topics
Truth table
Basic gates and operation
Boolean constant, variables, and theorems
Implementing circuit from Boolean expression

## Slide 4: Truth Table
Describe the outputs for any possible inputs of a system or circuit
Truth Table also shows the operation or function of a system
Number of entries correspond to where n is the number of inputs.
2 inputs truth table

## Slide 5: Basic gates and operation Inverter (NOT)
Single input and single output
Expression :
Operation : inversion or complement
Also call NOT gate
A
X
Truth table

## Slide 6: Basic gates and operation OR Gate
Can have two or more inputs and single output
Expression :
Operation : Logical addition
Outputs are LOW when all inputs are LOW
Truth table

## Slide 7: Basic gates and operation AND Gate
Can have two or more inputs and single output
Expression :
Operation : Logical multiplication
Outputs are HIGH when at All inputs are HIGH
Truth table
X = A.B

## Slide 8: Basic gates and operation NOR Gate
Can have two or more inputs and single output
Expression :
Operation : Inverted OR Gate
Outputs are HIGH when at all inputs are LOW
Truth table

## Slide 9: Basic gates and operation NAND Gate
Can have two or more inputs and single output
Expression :
Operation : Inverted AND Gate
Outputs are LOW when at least one inputs are HIGH
Truth table

## Slide 10: Basic gates and operation Exclusive-OR Gate (XOR)
Can have two or more inputs and single output
Expression :
Operation : Outputs are HIGH when input are opposites
Truth table

## Slide 11: Basic gates and operation Exclusive-NOR Gate (XNOR)
Can have two or more inputs and single output
Expression :
Operation : Outputs are HIGH when input are the same
Truth table

## Slide 12: Boolean Operations
Boolean Algebra is the mathematics of digital systems
Terms in Boolean Algebra:
  Variable: symbol to represent an action, a condition, or data
  Complement: inverse of a variable
    Ex: complement of variable A is Ā
  Literal: variable or complement of variable

## Slide 13: Boolean Addition
Equivalent to the OR operation
In logic circuits, a sum term (sum of literals) is produced by an OR operation with no AND operations involved
Sum term = 1 : when at least one of the literals is 1
Figure 8: Basic rules of Boolean addition
Examples of sum terms

## Slide 14: Boolean Multiplication
Equivalent to AND operation
In logic circuits, a product term (product of literals) is produced by an AND operation with no OR operations involved
Product term = 1: only if all literals in the term is 1
Figure 8: Basic rules of Boolean multiplication
Examples of product terms

## Slide 15: Boolean Theorems
Single variable *x=0 or 1
x . 0 = 0
x . 1 = x
x . x = x
x . x = 0
x + 0 = x
x + 1 = 1
x + x = x
x + x = 1

## Slide 16: Boolean Theorems
Multivariable Theorems
x + y = y + x
x . y = y . x
x + (y + z) = (x + y) + z = x + y + z
x(yz) = (xy)z = xyz
a) x(y+z) = xy + xz
  b) (w+x)(y+z) = wy + xy + wz + xz
x + xy = x
  x + xy = x + y
  x + xy = x + y
Commutative Laws
Associative
Laws
Distributive Law

## Slide 17: Commutative Laws
The order in which the variables are ORed makes no difference
The order in which the variables are ANDed makes no difference

## Slide 18: Associative Laws
When ORing more than 2 variables, the result is the same regardless
of the grouping of the variables
It makes no difference in what order the variables are grouped when
ANDing more than 2 variables

## Slide 19: Distributive Law

## Slide 20: Rules of Boolean Algebra
Rule1: Anything ANDed with 0 is equal to 0
Rule2: Anything ANDed with 1 is equal to itself

## Slide 21: Rules of Boolean Algebra
Rule3: Anything ANDed with itself is equal to itself
Rule4: Anything ANDed with its own complement is equal to 0

## Slide 22: Rules of Boolean Algebra
Rule5: Anything ORed with 0 is equal to itself
Rule6: Anything ORed with a 1 is equal to 1

## Slide 23: Rules of Boolean Algebra
Rule7: Anything ORed with itself is equal to itself
Rule8: Anything ORed with its own complement is equal to 1

## Slide 24: Rules of Boolean Algebra
Rule 9: Anything complemented twice will return to its original logic level

## Slide 25: Proof of logic circuit simplification
Example: Proof the following expression
  Solution: construct a truth table
A | B | D | AB’D | AB’D’ | AB’D+AB’D’ | AB’
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 26: References
  T. Floyd, “Digital Fundamental”, 10th Ed., USA : Prentice-Hall, 2008.
  R.J. Tocci, “Digital Systems: Principles and Applications”, 10th Ed., USA : Prentice-Hall, 2006.

## Slide 27: Norazian Subari Fakulti Kejuruteraan Elektrik & Elektronik Universiti Malaysia Pahang 26600 Pekan, Pahang, Malaysia http://fkee.ump.edu.my/index.php/en/staff-menu/articles-staff/1622-norazian-subari-main-profile