## Slide 1: IMAGE PROCESSING INTRODUCTION TO DIGITAL IMAGE PROCESSING
By
DR. FERDA ERNAWAN
Faculty of Computer Systems & Software Engineering ferda@ump.edu.my

## Slide 2: Today’s Lecture
This lecture will cover:
  Digital Image
  Image Types
  Image Processing Applications
  Image Processing Procedures
Learning Outcomes:
  To introduce digital image processing.
  Expose with image processing application.
  Familiar with image processing methodology

## Slide 3: Image Processing
A digital image consists of pixel values that represents the brightness. In order to convert an analog image into a digital image, sampling and quantization process are required in digitalization which illustrate as follows:
Analog Image
Sampling
Quantization
Digital Image
Digital image from analog image
Images taken from Gonzalez and Woods, 2016

## Slide 4: Origin of image Processing
Media industry (1921):
  Digital images were transmitted through undersea cables, and then printed by telegram printers.
Images taken from Gonzalez and Woods, 2016

## Slide 5: Soar Into Outer Space
Taken by space probe in 1964 Picture made with a1964. Picture made with a television camera (vidicon), transmitted to the earth by analog modulation, and digitized on the ground.
Moon picture by US spacecraft
Images taken from Gonzalez and Woods, 2016

## Slide 6: Image Types
Digital images are categories as follows (Jayaraman, Veerakumar, Esakkirajan, 2017):
  Binary image
  Grayscale image
  Color image
  False-color image or Pseudo-color image
  Multi-spectral image
  Thematic image
  Video Image

## Slide 7: Image Types
Binary image
An image has only two possible pixel values, 0 or 1.
Grayscale image
Grayscale image is typically stored with 8-bits per pixel, which allows 256 intensities.
Thematic image
Image products of classification processing of multispectral image of any terrain.
Video image
a three-dimensional generalization of still images, where third dimension is time.

## Slide 8: Image Types
Color image
A digital image that includes color informations for each pixel.
False-color image
An image derived from mapping each pixel value to a color image based on a table or function.
Multi-spectral image
An image of the same object (earth or planetary surface), taken in different bands of visible of electromagnetic spectrum

## Slide 9
Image Processing Applications

## Slide 10: Medical Images
Heart Image
Edge Detection
Images taken from Gonzalez and Woods, 2016

## Slide 11: Multispectral Satellite
LANDSAT satellite images of the Washington DC area
(Image courtesy of NASA)
Images taken from Gonzalez and Woods, 2016

## Slide 12: Image Processing in Manufacturing
Some examples of image processing in manufacturing (a) Packaged pills (b) Bottles (c) A circuit board
a
b
c
Images taken from Gonzalez and Woods, 2016

## Slide 13: Motion Pictures

## Slide 14: Law Enhancement and Biometrics
  Automated toll systems using plate recognition
  Plate detection for speed cameras
  Video surveillance
  Enhancement security using fingerprint

## Slide 15: Remote Sensing
Hurricane Andrew taken by NOAA GEOS
Images taken from Gonzalez and Woods, 2016

## Slide 16: Beyond Visible of Thermal Images
Human body disperses heat (red pixels)

## Slide 17: Image Processing Procedures
Images taken from Gonzalez and Woods, 2016

## Slide 18: Image Aquisition
Images taken from Gonzalez and Woods, 2016

## Slide 19: Image Enhancement
Images taken from Gonzalez and Woods, 2016

## Slide 20: Image Restoration
Image Acquisition
Image Restoration
Morphological Processing
Segmentation
Representation & Description
Image Enhancement
Object Recognition
Problem Domain
Colour Image Processing
Image Compression
Images taken from Gonzalez and Woods, 2016

## Slide 21: Image Restoration
Images taken from Gonzalez and Woods, 2016

## Slide 22: Morphological Processing
Images taken from Gonzalez and Woods, 2016

## Slide 23: Segmentation
Images taken from Gonzalez and Woods, 2016

## Slide 24: Object Recognition
Images taken from Gonzalez and Woods, 2016

## Slide 25: Representation & Description
Images taken from Gonzalez and Woods, 2016

## Slide 26: Image Compression
Images taken from Gonzalez and Woods, 2016

## Slide 27: Colour Image Processing
Images taken from Gonzalez and Woods, 2016

## Slide 28: References
R.C. Gonzalez and R.E. Woods, 2016. Digital Image Processing, Pearson Education India; Third edition.
A.K. Jain, 2015. Fundamentals of Digital Image Processing, Pearson Education India; First edition.
R.C. Gonzalez, R.E. Woods and S.L. Eddins, 2017. Digital Image Processing Using MATLAB. McGraw Hill Education; 2 edition.
S. Jayaraman, T. Veerakumar, S. Esakkirajan, 2017.Digital Image Processing, McGraw Hill Education; 1 edition.