## Slide 1: Electric and Electronic Technology Chapter 2C – Resistance in Series and Parallel
by
Akhtar Razali FKM akhtar@ump.edu.my

## Slide 2: Chapter Description
Aims
  To understand what is voltage divider, analysis and its application
  To understand what is current divider, analysis and its application
Expected Outcomes
  Student should be able to identify voltage and current divider circuit.
  Able to solve problem related to voltage and current divider
Other related Information
  One of mid semester exam is from this topic
  No other relevant information be disclosed
References
  Rizzoni G., 2004, Principles and Applications of Electrical Engineering, Revised Fourth Edition, Fourth Edition, McGraw Hill
  Hambley A.R., 2005, Electrical Engineering Principles and Applications, Third Edition, Pearson Prentice Hall

## Slide 3: Contents
Voltage divider circuit
Current divider circuit

## Slide 4: Voltage Divider
When a voltage is applied to a series combination of resistances, a fraction of voltage appears across each of the resistance.
A series circuit acts as a voltage divider. The voltage divider is an important application of series circuits.
A circuit consisting of a series string of resistors connected to a voltage source act as voltage divider.

## Slide 5: Voltage Divider Formula
Assume a circuit with n resistors in series as shown in Figure where n can be any number.
Source: Rizzoni

## Slide 6: Voltage Divider Formula
Let Vx represent the voltage drop across anyone of the resistors and Rx represent the number of a particular resistor or combination of resistors.
By Ohm's law, you can express voltage drop across Rx as follows:
Vx = IRx

## Slide 7: Voltage Divider Formula
The current through the circuit is equal to the source voltage divided by the total resistance (I= Vs/RT). In the circuit of Figure, the total resistance is R1+R2+R3 + ... + Rn.
By substitution of Vs/RT for I in the expression for Vx,
Vx=(Vs/RT)Rx

## Slide 8: Voltage Divider Formula
Rearranging the terms, you wil get,
Vx=(Rx/RT)Vs

## Slide 9: Voltage Divider by Definition
Therefore,
“The voltage drop across any resistor or combination of resistors in a series circuit is equal to the ratio of that resistance value to the total resistance, multiplied by the source voltage.”

## Slide 10: Example – Voltage Divider Problem
Source: Rizzoni

## Slide 11: Example – Voltage Divider Problem (Solution)
Source: Rizzoni

## Slide 12: Example 2
Source: Rizzoni

## Slide 13: Solution for Example 2
Source: Rizzoni

## Slide 14: Exercise 1
use the voltage-division principle to calculate v
Source: Rizzoni

## Slide 15: Exercise 2
A source supplies 120V to the series combination of a 10 Ohm Resistance, a 8 Ohm Resistance, and an unknown resistance Rx. The voltage across the 8 Ohm Resistance is 20 V. Determine the value of the unknown resistance.

## Slide 16: Exercise 3
Determine the voltage between the following points in the voltage divider of below circuit.
a) A to B
b) A to C
c) B to C
d) B to D
e) C to D
Source: Rizzoni

## Slide 17: Current Divider
In a parallel circuit, the total current into the junction of the parallel branches divides among the branches. Thus, a parallel circuit acts as a current divider. This current-divide principle is illustrated in next Figure for a two-branch parallel circuit in which part of the total current IT goes through R1 and part through R2.

## Slide 18: Example
Source: Rizzoni

## Slide 19: Current Divider Formula
Source: https://commons.wikimedia.org/wiki/File:Current_division_example.svg

## Slide 20: Current Divider Formula
The current through any one of the parallel resistors is Ix, where x represents the number of a particular resistor (l, 2, 3, and so on).
By Ohm's law, you can express the current through any one resistors in previous Figure as follows:
Ix=(Vs/Rx)

## Slide 21: Current Divider Formula
The source voltage, Vs, appears across each of the parallel resistors, and Rx represents any one of the parallel resistors. The total source voltage, Vs, is equal to the total current times the total parallel resistance.
Vs=IT.RT

## Slide 22: Current Divider Formula
Substituting ITRT for Vs in the expression for Ix results in
Ix=(ITRT)/Rx
Rearranging the formula,
Ix=(RT/Rx).IT
where x = 1,2,3, etc.

## Slide 23: Current Divider Definition
Therefore,
“The current (Ix) through any branch equals the total parallel resistance (RT) divided by the resistance (Rx) of that branch, and then multiplied by the total current (IT) into the junction of parallel branches. “

## Slide 24: Example
Source: https://commons.wikimedia.org/wiki/File:Two_Resistors_in_Parallel.svg

## Slide 25: Solution
Source: Rizzoni

## Slide 26: Conductance in Parallel
Source: Rizzoni

## Slide 27: Example
Source: Rizzoni

## Slide 28: Solution
Source: Rizzoni

## Slide 29
Determine the current through each resistor in the circuit of below Figure.
Source: Rizzoni

## Slide 30
RT=(R1R2)/(R1+R2)
Source: Rizzoni

## Slide 31: Current Divider Other Formula – for 2 resistors only
Using the general current divider formula, the formula for I1 and I2 can be written as;
I1= (RT/R1)IT
and
I2= (RT/R2)IT

## Slide 32: Current Divider Other Formula – for 2 resistors only
substitute RT in above formulas, we will obtain current-divider formulas for the special case of two branches, which are;
I1= (( R2/(R1+R2)) IT
and
I2= (( R1/(R1+R2)) IT

## Slide 33: Exercise
Find I1 and I2,
Source: Rizzoni

## Slide 34: Conclusion of The Chapter
Conclusion #1
  Voltage divider is represented by a series circuit.
  Current divider is represented by a parallel circuit.

## Slide 35: Akhtar Razali FKM, UMP.