## Slide 1: Electric and Electronic Technology Chapter 3A – Capacitance
by
Akhtar Razali FKM akhtar@ump.edu.my

## Slide 2: Chapter Description
Aims
  Determine current, voltage, power and energy for capacitor.
Expected Outcomes
  Students able to understand how capacitance works, its application and related analysis
Other related Information
  One question for final exam is from this topic
  No other relevant information be disclosed
References
  Rizzoni G., 2004, Principles and Applications of Electrical Engineering, Revised Fourth Edition, Fourth Edition, McGraw Hill
  Hambley A.R., 2005, Electrical Engineering Principles and Applications, Third Edition, Pearson Prentice Hall

## Slide 3: Contents
Determine the current, voltage, power and energy for a capacitance or inductance.
Determine the equivalent capacitance and inductance from combination of series and parallel of capacitance and inductance.

## Slide 4: Capacitance
A capacitor is basically a device which stores an electric charge. Physically, it consists of two metal plates separated by insulating material or dielectric
Image source: https://commons.wikimedia.org/wiki/File:Parallel_plate_capacitor.svg

## Slide 5: Capacitance
Application of a DC voltage across the capacitor produces deficiency of electrons on the positive plate and excess of electrons on the negative plate
Image source: https://commons.wikimedia.org/wiki/File:Capacitor_schematic.svg

## Slide 6: Capacitance
In an ideal capacitor, the stored charge q is proportional to the voltage between the plates:
q = C.v
the constant proportionality is the capacitance C, which has units of farads (F).
Farads are equivalent to coulomb/volt

## Slide 7: Current and Voltage for a capacitance
Current at capacitor is the time rate of flow of charge
i = dq/dt
= d (Cv)/dt
= C . dv/dt

## Slide 8
If the current (i) flowing through a capacitance C, we can calculate voltage (v) at the capacitor.
Image source: Rizzoni

## Slide 9: Example 1 - Capacitance
Suppose voltage v(t) in below figure is applied to a 1uF capacitance. Plot the stored charge and current passing through the capacitance vs. time

## Slide 10: Example 1- capacitance
Source: Rizzoni

## Slide 11: Example 2

## Slide 12: Example 2

## Slide 13: Example 2

## Slide 14: Power and energy for capacitance
The power delivered to a circuit element is the product of the current and the voltage.
P = V . I = V. (C . dv/dt)
If we integrate the power delivered from t0 to t, we find energy delivered.
Source: Rizzoni

## Slide 15: Energy
Source: Rizzoni

## Slide 16: Example 2
Suppose the voltage form in the plot is applied to a 10uF capacitor. Find the current , energy and stored charge plots
Source: Rizzoni

## Slide 17: Example 2
Source: Rizzoni

## Slide 18: Example 2
Source: Rizzoni

## Slide 19: Example 2
Capacitance in parallel connection is expressed by:
  Ceq = C1 +C2 +C3
  Apply KCL at the top node, then:
Source: Rizzoni

## Slide 20: Capacitance in parallel connection
Source: Rizzoni

## Slide 21: Capacitance in Series Connection
Source: Rizzoni

## Slide 22: Exercise 1
Find equivalent capacitance in below circuit.
Source: Rizzoni

## Slide 23: Conclusion of The Chapter
Conclusion #1
  Capacitor is used in many application that deal with steady current and voltage constant.
Conclusion #2
  Series equivalent capacitance is identical to the way we calculate resistor on series.

## Slide 24: Akhtar Razali FKM, UMP.