## Slide 1: Electric and Electronic Technology Chapter 4A – Magnetic Field and Transformer
by
Akhtar Razali FKM akhtar@ump.edu.my

## Slide 2: Chapter Description
Aims
  To understand the principle of magnetic field
  To understand the principle element and working principle of a transformer
Expected Outcomes
  Students able to understand how magnetic field works, its application and other related analysis
  Students able to understand how transformer works, its application
Other related Information
  One question for final exam is from this topic
  No other relevant information be disclosed
References
  Rizzoni G., 2004, Principles and Applications of Electrical Engineering, Revised Fourth Edition, Fourth Edition, McGraw Hill
  Hambley A.R., 2005, Electrical Engineering Principles and Applications, Third Edition, Pearson Prentice Hall

## Slide 3: Contents
Working principle of magnetic field.
Principle element of a transformer, working principle and its application.

## Slide 4: Direction of the Field of a Long Straight Wire
A current-carrying wire produces a magnetic field
Right Hand Rule
  Grasp the wire in your right hand
  Point your thumb in the direction of the current
  Your fingers will curl in the direction of the field
The magnitude of the field at a distance r from a wire carrying a current of I is:
Image source: https://commons.wikimedia.org/wiki/File:V-1_right_hand_thumb_rule.gif
µo = 4  x 10-7 T.m / A
  µo is called the permeability of free space

## Slide 5: Electromagnet concept
An electromagnet consists of an iron core placed inside a wire coil. The magnetic field strength of a wire coil carrying an electric current increases in direct proportion to the number of turns of the coil
Image source: https://commons.wikimedia.org/wiki/File:VFPt_cylindrical_coil_real.svg

## Slide 6: Transformer
An A.C. device used to change high voltage low current A.C. into low voltage high current A.C. and vice-versa without changing the frequency
In brief,
1. Transfers electric power from one circuit to another
2. It does so without a change of frequency
3. It accomplishes this by electromagnetic induction
4. Where the two electric circuits are in mutual inductive influence of each other.

## Slide 7: TRANSFORMER USES
Impedance matching
Electrical Isolation
AC power transmission
    STEP-UP Transformer
    STEP-DOWN Transformer

## Slide 8: INDUCTION THEORY
Transformers behaviour is based on Faraday’s Law of Induction
Where:-
ε – EMF (V)
N – No of turns of wire
ΦB – Magnetic flux (Wb)

## Slide 9: INDUCTION THEORY
Image source: https://en.wikipedia.org/wiki/Transformer

## Slide 10: Working Principle of a Transformer
1. When current in the primary coil changes being alternating in nature, a changing magnetic field is produced
2. This changing magnetic field gets associated with the secondary through the soft iron core
3. Hence magnetic flux linked with the secondary coil changes.
4. Which induces e.m.f. in the secondary.

## Slide 11: TRANSFORMER MODELS
Np = No of windings on the primary Ns = No of windings on the secondary
ip = Current into the primary is = Current out from the secondary
Vp = Voltage across the primary Vs = Voltage across the secondary
Image source: https://en.wikipedia.org/wiki/File:Ideal_Transformar.png

## Slide 12: Primary and Secondary Relationship
Turns ratio (a) is defined as the ratio of the number of turns in the secondary winding (Nsec) to the number of turns in the primary winding (Npri).
VP = NP = iS = a
VS NS iP
Note; a < 1 = Step up transformer
a > 1 = Step down transformer
Voltage and current angles are NOT affected hence,
θP = θS = θ

## Slide 13: Losses in a Transformer
Transformers have losses and these losses must come into consideration.
    Copper losses (I^2 R)
    Leakage Flux losses
    Core losses
        Eddy currents
        Hysteresis losses

## Slide 14: REAL TRANSFORMER LOSSES
    Copper losses (I^2 R)
    Leakage Flux losses
    Core losses
        Eddy currents
        Hysteresis losses

## Slide 15: EFFICIENCY
Efficiency (η) is the ratio of the power out to the power in of a transformer.
  η in an Ideal transformer, no power losses
    PIN = VP IP cos θP
    POUT = VS IS cos θS
    PIN = POUT = VP IP cos θP = VS IS cos θS
    ηIdeal = 100%

## Slide 16: Voltage Regulation
Voltage regulation (VR) is the ability of a system to provide near constant voltage over a wide range of load conditions. Also it compares the VO at no load to VO at full load.
An Ideal transformer has a voltage regulation,
VR = 0%
Reference : http://en.wikipedia.org/wiki/Voltage_regulation

## Slide 17: Conclusion of The Chapter
Conclusion #1
  The strength of magnetic field is proportional to the increasing number of conductor used in a system.
Conclusion #2
  Transformer is one of many application of magnetism.

## Slide 18: Akhtar Razali FKM, UMP.