## Slide 1: Electric and Electronic Technology Chapter 5A – Op-Amp
by
Akhtar Razali FKM akhtar@ump.edu.my

## Slide 2: Chapter Description
Aims
  To understand the principle of Op-Amp
  To understand the application and analysis of various type of op-amps
Expected Outcomes
  Students able to understand how Op-Amp works, its application and other related analysis
  Students able to distinguish various type of op-amp and its application
Other related Information
  One question for final exam is from this topic
  No other relevant information be disclosed
References
  Rizzoni G., 2004, Principles and Applications of Electrical Engineering, Revised Fourth Edition, Fourth Edition, McGraw Hill
  Hambley A.R., 2005, Electrical Engineering Principles and Applications, Third Edition, Pearson Prentice Hall

## Slide 3: Contents
Describe the operation of the operational amplifier principles and characteristics.
Analyze the inverting and non-inverting operational amplifier circuits.

## Slide 4: Op-Amp Introduction
An operational amplifier is an integrated circuit, that is, a large collection of individual electrical and electronic circuits integrated on a single silicon wafer.
An operational amplifier — op-amp — can perform a great number of operations, such as addition, filtering, or integration, which are all based on the properties of ideal amplifiers and of ideal circuit elements. The introduction of the operational amplifier in integrated circuit form marked the beginning of a new era in modern electronics.

## Slide 5: Op-Amp in Real
Source: https://commons.wikimedia.org/wiki/File:Op-amps.jpg

## Slide 6: Op-Amp Pinout
Source: https://commons.wikimedia.org/wiki/File:Generic_741_pinout_top.png

## Slide 7: Ideal Op-Amp
Infinite voltage gain, Av = ∞
Infinite input impedance, Zin = ∞
Zero output impedance, Zout = 0.
However, the ideal op-amp can never be made.
Because any device has limitations: current, voltage are limited.

## Slide 8: Typical Ranges of Op-Amp
Source: Rizzoni

## Slide 9: Inverting Op-Amp
Source: https://commons.wikimedia.org/wiki/File:Op-Amp_Inverting_Amplifier_KCL.svg

## Slide 10: Inverting Op-Amp
Source: Rizzoni

## Slide 11: Example
If R1 = 100 ohm, Rf = 200 ohm and Vi = 10 V
Such that:
Vo = -(Rf/R1).Vi
= - (200/100)10 = - 20 V
And current through R1 is:
i = (Vi – 0)/ R1 = 10/100 = 0.1 amp

## Slide 12: Exercise 1
Source: Rizzoni

## Slide 13: Summing Op-Amp
Source: Rizzoni

## Slide 14: Example
Source: Rizzoni

## Slide 15: Example
If Rf = 100 ohm, Ra = 200 ohm, Rb = 100 ohm and VA = VB = 10 V
Such that:
Vo = -(Rf/RA).VA - (Rf/RB).VB
= - (100/200)10 - (100/100)10 = - 15 V

## Slide 16: Exercise 1
Source: Rizzoni

## Slide 17: Example 1 - Solution
Source: Rizzoni

## Slide 18: Exercise 1
Source: Rizzoni

## Slide 19: Exercise 2
Source: Rizzoni

## Slide 20: Non-inverting Amplifier
Source: Rizzoni

## Slide 21: Non-Inverting Op-Amp Formula
Source: Rizzoni

## Slide 22: Example 1
If R1 = 100 ohm, Rf = 200 ohm and Vi = 10 V
Such that:
Vo = (1 + Rf/R1).Vi
= (1 + 200/100)10 = 30 V

## Slide 23: Various Type of Op-Amp
Source: Rizzoni

## Slide 24: Conclusion of The Chapter
Conclusion #1
  Inverting Op-Amp produces inverting output while at the same time amplifies the output voltage.
  Non-inverting Op-Amp does not inverts output but amplifies the output voltage
  Summing Op-Amp added up the Op-Amp and amplifies output voltage.
  KCL is used to derive the equation for each Op-Amp.

## Slide 25: Akhtar Razali FKM, UMP.