## Slide 1: BSB3503 - Biomanufacturing CHAPTER 2 Process Plant Design – Part III
Author: Nurul Azyyati Sabri
Co-Author / Editor: Rama Yusvana Faculty Industrial Sciences & Technology yusvana@ump.edu.my

## Slide 2: Basic flow diagram

## Slide 3: Production of Ethane from Ethanol
Ethanol is feed to continuous reactor with presence of Acid Sulphuric catalyser to produce ethylene. Distillation process then will be applied to separate ethylene-H2O mixture. Ethylene as a top product is then condensate with condenser to perform liquid ethylene. Hydrogenation of ethylene applies in another reactor with presence of Nickel catalyzer to produce ethane as a final product.

## Slide 4: Production of Ethane from Ethanol

## Slide 6: Process flow diagram (PFD)
Showing the connectivity of all the streams of materials and the equipment
PFD will contains the following information:-
All equipments : such as pumps and valves, compressors, columns.
All utility streams such as steam lines, compressed air lines, electricity, etc.
All process flow streams: identified by a number, process condition, chemical composition.
Basic control loops: showing the control strategy used

## Slide 7
Using software – AUTOCAD and VISIO
Developed special for process engineering
Typical component data in the software:
  Instrument ID
  Drawing number
  Dimensions

## Slide 8
Process Unit Symbology
Symbol
Description
Heat exchanger
H2O
Water cooler
S
Steam heater
Cooling coil
The Process Flow Diagram (PFD)

## Slide 9
Process Unit Symbology
Symbol
Description
Heater coil
Centrifugal pump
Turbine type compressor
Pressure gauge
The “Process Flow Diagram” (PFD)

## Slide 10
Process Unit Symbology
Symbol
Name
Stripper
Absorber
Convert liquid mixture into gas phase
Description
Convert mixture gas into liquid phase
The “Process Flow Diagram” (PFD)

## Slide 11
Process Unit Symbology
Symbol
Name
Distillation
column
Liquid mixer
Separate liquid into miscellaneous component fractions.
Description
Mix liquid components.
or
The “Process Flow Diagram” (PFD)

## Slide 12
Process Unit Symbology
Symbol
Name
Reaction
chamber
Horizontal tank
or cylinder
Location of chemical process or reaction occurs
Description
Store liquid or gas.
The ”Process Flow Diagram” (PFD)

## Slide 13
Process Unit Symbology
Symbol
Name
Boiler
Centrifuge
Heating purposes.
Description
Physically separated liquid mixture (exp: oil-liquid)
The “Process Flow Diagram” (PFD)

## Slide 14
Valve Symbology
Symbol
Name
Gate Valve
Check Valve
The “Process Flow Diagram” (PFD)
Globe Valve
Ball Valve
Butterfly Valve

## Slide 15
Valve Symbology
Symbol
Name
Relief Valve (d)
Angle Valve (e)
The “Process Flow Diagram” (PFD)
Needle Valve (a)
3-Way Valve (c)
Butterfly Valve (b)
(a)
(c)
(b)
(d)
(e)

## Slide 16
Line Numbering and Method for Drawing
- Generally numbers made from left to right.
- Horizontal lines cuts or break vertical line.
Yes
No
No
The “Process Flow Diagram” (PFD)
PFD will contains the following information:-
All process flow streams: identification by a number, process condition, chemical composition.

## Slide 17: Example

## Slide 18
Stream Description
The Process Flow Diagram (PFD)
- Mainly reactors and towers, etc.
Use Flags when necessary
Can include full stream data

## Slide 19
The Process Flow Diagram (PFD)

## Slide 20: Example

## Slide 21
Stream Number | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Temperature (oC) | 25.0 | 35.0 | 35.0 | 35.0 | 35.0 | 60.3 | 41 | 38 | 54.0 | 45.1
Pressure (psi) | 28 | 32.2 | 31.0 | 31.0 | 30.2 | 45.1 | 31.3 | 24.0 | 39.0 | 2.6
Vapor fraction |  |  |  |  |  |  |  |  |  | 
Stream Information - Full stream data

## Slide 22: Example

## Slide 23: The Process Flow Diagram (PFD)
PFD usually also contains the following information:-
Basic control loops: showing the control system in place.

## Slide 25: Piping and instrumentation diagrams
The drawing is started after the order placement and approximately at the same time to the procurement of the components.
The information given is subdivided into basic information.

## Slide 26
Information includes:
  Appliances and machinery
  Pipes or means of transport (e.g. moving belts)
  Valves and fittings
  Information on dimension, nominal pressures and material classification
  Any insulation, electric pipe heater, gradients & materials

## Slide 27
Example:
  Simple pump group
  Atmosphere Vessel
  Pump unit with automatic flushing device
  Tubular heat exchanger
  Hydrochloric acid metering system

## Slide 28: Example: Simple pump group

## Slide 29: Main apparatus
Steps in procurement of the main apparatus:
1) process-related design
  Applied knowledge of thermal, chemical, mechanical, biological process engineering.
  Hydrodynamic: The reactor diameter and its height, Heat exchangers, Design of compressors: thermodynamic aspect
  All results recorded in technical data sheet

## Slide 30
2) strength related design
  Calculation on wall thickness
3) production-related design
  Carried out within detail engineering
  Assigned to subcontractors

## Slide 31: Layout
Generally very complex
Occur only after submission of P&I drawing – within the detail engineering

## Slide 32: Quotation
A request for quotation (RFQ) is a standard business activity inviting suppliers to bid specific products or services.
Include payment terms, quality level per item or contract length etc.
To receive accurate quotation, therefore it also includes the full specifications of the items/services.

## Slide 33: Quotation
The more detailed the specifications should minimize potential problems regarding products or services specification.
Acting as legal binding documentation for the suppliers.
Best suited for products and services that are as standardised to make each supplier's quote comparable.