## Slide 1: BSB3503 - Biomanufacturing CHAPTER 11 GMP – Pharmaceutical Water
Author: Nurul Azyyati Sabri
Co-Author / Editor: Rama Yusvana Faculty Industrial Sciences & Technology yusvana@ump.edu.my

## Slide 2: Introduction
Pharmaceutical water need to comply with the pharmacopoeias requirements (compendial water):
If the water having specific characteristic defined for a specific process, falls below the Pharmacopoeias limits -> non compendial water.
Water can be used as Active Pharmaceutical Ingredients (APIs)

## Slide 3: Introduction
Most widely used  high cost
The percentage of water in finished products between 0 - 90%.
Subject to current Good Manufacturing Practices (cGMPs) regulation.

## Slide 4: Pharmaceutical Water
Water can be used during the development, in manufacturing and in the preparation of drugs.
These waters are divided into two categories:
1. COMPENDIAL WATER
2. NON-COMPENDIAL WATER

## Slide 5: 1. COMPENDIAL WATER
Compendial waters meet the USP, EP (European Pharmacopoeia) and JP (Japan Pharmacopoeia) requirements
However, according to FDA, the document notes that: “(…) the specifications outlined in the monographs (USP, EP end JP) are the minimum requirements for compendial water.
Additional specifications may be added or combined based on process requirements”.

## Slide 6: Types of Compendial Water
According to USP, EP and JP monographs the types include:
PW (Purified Water)
WFI (Water For Injection)
HPW (Highly Purified Water) – EP monograph only
WFH (Water For Hemodialysis) – USP monograph only.

## Slide 7: PW (Purified Water)
Purified Water is classified for pharmaceutical use as an excipient in the production of non-parenteral preparations and in specific pharmaceutical preparations/tests and assays, for which water is indicated, unless otherwise specified (see related USP, EP and JP pharmacopeia for reference).

## Slide 8: PW (Purified Water)
Drinking water is the minimal source of feed water to produce PW, through deionization, distillation, ion exchange, reverse osmosis, filtration or other appropriate procedures. PW is also a starting material in the WFI and pure steam preparations.

## Slide 9: WFI (Water For Injection)
Water For Injection is classified for pharmaceutical purposes as an excipient in the production of parenteral preparations and in other pharmaceutical preparations where the endotoxin content must be verified (see related USP, EP and JP pharmacopeia for reference).

## Slide 10: WFI (Water For Injection)
Deionized water (that may be pre-treated for subsequent distillation or appropriate process) is the minimal source of feed water to produce WFI.
In addition to the PW specifications, WFI adds the test for Bacterial endotoxins and complies with all requirements (except for Labeling) for the packaged water know as “Sterile Purified Water” (see USP monograph).

## Slide 11: WFI Production Technology
Vapor Compression Distillation (VC) System
The production process includes PW water evaporation followed by pure steam separation and condensation.

## Slide 12: WFI Production Technology
The steam is purified using centrifugal and gravity separation methods. This system produces dry, saturated steam and the condensate meets the requirements of international pharmacopoeias for Water-for-Injection

## Slide 13: Advantages VC Technology
Low energy consumption
No need of cooling water to condensate the pure steam
No need for high quality inlet water (in some cases even softened water can feed the VC still)
Very high quality of the WFI due to the strong degassing process

## Slide 14: Advantages VC Technology
No need to pressurize the inlet water
WFI outflow at high pressure (1 – 1.5 bar) without any additional pump
Extremely safe process, with no risk of any cross contamination through plant steam or inlet water
Highest flexibility in terms of capacities and WFI temperatures
Reduced Maintenance

## Slide 15: HPW (Highly Purified Water), as defined by EP monograph;
Highly Purified Water is classified (see EP monograph) as an excipient in the production of pharmaceutical products where bacterial endotoxins need to be controlled, unless WFI specified, i.e. for example WFI.

## Slide 16: WFH (Water For Hemodialysis), as defined by USP monograph
Water For Hemodialysis is primarily classified in pharmaceutical purposes for hemodialysis applications, i.e. in the diluition of concentrate solutions.
The feed to the filtration unit is made from EPA (US Environmental Protection Agency) drinking water which has been further purified to reduce chemical and microbiological components. Note that WFH is not intended for injection.

## Slide 17
Derived from “21 CFR Part 211: Current Good Manufacturing Practices for Finished Pharmaceuticals”.
  “General statements relate to the requirement for water used in production or cleaning processes to not alter the safety, identity, strength, quality or purity of the drug product.”
  Subject to FDA scrutiny in the US.
GMP-Regulated Pharmaceutical Water

## Slide 18
Derived from “21 CFR Part 211: Current Good Manufacturing Practices for Finished Pharmaceuticals”.
  “All materials must be proven to be compatible with the product and process & does not contribute to contaminants”.
  Written records and procedures for these steps.
  All rinse and cleaning water qualities must be proven to be appropriate.

## Slide 19: 2. NON-COMPENDIAL WATER
Non-compendial waters meet, at least, the requirements of potable (drinking) water.
Non-compendial waters are not necessarily of lesser quality than compendial waters
However, non-compendial water systems may or may not be validated

## Slide 20: 2. NON-COMPENDIAL WATER
Generally, non-compendial waters are intended of the appropriate quality required by the single application.
Example of Non-compendial water: Potable Water, Softened water, Ultra Filtration water, Reverse Osmosis Water, DI (Deionization process) water, Distilled water

## Slide 21
A function of several factors such as where the product will be shipped.
Microbial control methods.
Aspects of Pharmaceutical Water

## Slide 22
The chemical attributes.
The capital and operating costs for pharmaceutical water systems can vary significantly.
Water for injection (WFI) systems have fewer acceptable options for generation, storage, and distribution.
Aspects of Pharmaceutical Water

## Slide 23
Sanitization method, storage and distribution equipment
Thermally sanitizable systems generally have higher capital costs.
Aspects of Pharmaceutical Water

## Slide 24
Chemically sanitized equipment may have a lower capital cost
Aspects of Pharmaceutical Water

## Slide 25: Water Quality Sampling
Must be developed to monitor system operation and control.
It is important to design sampling points into the unit processes.

## Slide 26: Water Quality Sampling
Test protocols and frequency.
Collected in an appropriate manner.
From actual production hoses.

## Slide 27: Validation
All pharmaceutical water systems need to be validated.
Meet specification of the water system.
All equipment suppliers, must be aware of the requirements for documentation for validation.