## Slide 1: BTV2213 Thermodynamics Chapter 2: Problem-Solving Technique
by
Nasrin Khodapanah
Faculty of Engineering Technology nasrin@ump.edu.my
For uploaded version, please click on this:
http://ocw.ump.edu.my

## Slide 2: Chapter Description
Aims
  Develop the concept of property, state, equilibrium, process and path in thermodynamics
  Discuss thermodynamics problem-solving technique
  Evaluate appropriate system boundaries for analyzing a variety of thermodynamics components and system
Expected Outcomes
  Students able to understand the concept of property, state, equilibrium, process and path
  Students able to extend the basic concepts of thermodynamics to problem solving technique
  Students able to understand system boundaries for analyzing a variety of thermodynamics components and system
References
  Cengel, Y.A and Boles, M.A (2010),”Thermodynamics: An Engineering Approach(7th Edition)”, McGraw Hill, New York
  Cengel, Y.A (2012): Introduction to Thermodynamics and Heat Transfer, McGraw Hill, New York
  Robert Balmer (2011): Thermodynamics, Jaico Publication

## Slide 3: Thermodynamics problem-solving technique

## Slide 4: System and Control volume

## Slide 5: Classification of thermodynamics systems

## Slide 6: Classification of thermodynamics systems
GAS
2 kg
1 m3
GAS
2 kg
3 m3
CLOSED System
with Moving Boundary
OPEN System
Mass YES
Energy YES
ISOLATED System
m = const.
E = const.
Mass NO
Energy NO

## Slide 7: Classification of thermodynamics systems
In
Out
Imaginary Boundary
Real Boundary
BOUNDARY around of OPEN System is CONTROL SURFACE /CONTROL VOLUME.
Mass and Energy can pass through Control Volume Boundaries

## Slide 8: Thermodynamics property
Property: any measurable/observable characteristics of the substance when the system is in equilibrium state.
Intensive property:
Those properties do not depend on the mass, such as temperature, pressure and density.
Extensive property:
Those properties depend on the mass, such as volume, total energy and etc.

## Slide 9: State & Equilibrium
Those properties of system describe the condition of the system is system STATE
m = 2 kg
T1 = 25 ºC
V1 = 1 m3
STATE 1
STATE 2

## Slide 10: State & Equilibrium
EQUILIBRIUM (State of Balance)
Thermal Equilibrium :
NO Temperature Gradient throughout the system.
Mechanical Equilibrium :
NO Pressure Gradient throughout the system.
Phase Equilibrium :
System having more than 1 phase.
Mass of each phase is in equilibrium.
Chemical Equilibrium :
Chemical composition is constant
NO reaction occurs.

## Slide 11: Path and Process
Property A
State 1
State 2
Property B
Path
State 1
State 2
t=0
t=t1
t=0
t=t2t
t2 < t1
Quasi-Static
Non-Quasi-Static

## Slide 12: Path and Process

## Slide 13: Reversible / Irreversible Process

## Slide 14: Appropriate system boundaries to analyze a variety of thermodynamics components and system
TUTORIAL CHAPTER 1

## Slide 15: Exercise#1
Express a pressure of 75.2 kPa as a gage pressure. The local atmospheric pressure is 103.4 kPa.
Notice that the result is negative. This can also be read “28.2 kPa below atmospheric pressure” or “28.2 kPa vacuum.”

## Slide 16: Exercise#2
Express a gage pressure of –42.7 kPa as an absolute pressure.
Because no value was given for the atmospheric pressure, we will use patm=101 kPa:

## Slide 17: Conclusion of The Chapter 2

## Slide 18: Hae-Geon Lee (2012) Introduction. Materials Thermodynamics
Huang, Biao, Yutong Qi, and A. K. M. Murshed. "First Principle Modelling for Chemical Processes." Dynamic Modelling and Predictive Control in Solid Oxide Fuel Cells: First Principle and Data-Based Approaches: 11-29.
Kanoglu, Mehmet, Ibrahim Dincer, and Yunus A. Cengel. "Exergy for better environment and sustainability." Environment, Development and Sustainability 11.5 (2009): 971-988.