## Slide 1: GEOTECHNICAL ENGINEERING Lateral Earth Pressure of Soil
by
Dr. Amizatulhani Abdullah Faculty of Civil Engineering ad Earth Resources amizatulhani@ump.edu.my
For updated version, please click on
http://ocw.ump.edu.my

## Slide 2: Chapter description
Aims
  This chapter provides further discussion and explanation related to lateral earth pressure in soil.
Expected Outcomes
  Apply various method of analysis to analyze the lateral pressure in soil.
References
  Das, B.M., “Principles of Geotechnical Engineering, 7th edition”, Cengage Learning (2010).
  Coduto, D.P., “Geotechnical Engineering Principles and Practices”, Prentice Hall (1998).
  Liu, C. & Evett, J.B., “Soils and Foundations, 7th edition”, Prentice Hall (2008).
  Whitlow, R., “Basic Soil Mechanics”, Prentice Hall (2004).
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 3: Content
Rankine’s theory of lateral earth pressure
Coulomb’s theory of lateral earth pressure
Conclusion
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 4: Rankine’s lateral earth pressure
He simplified Coulomb’s theory for cases when the surface of the backfill is horizontal, the friction between the wall and the backfill is negligible and the retaining wall is vertical.
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah
William J.M. Rankine (1820-1872)
Notes: http://scienceworld.wolfram.com/biography/Rankine.html

## Slide 5
 coefficient of earth pressure at rest,
Ko = 1 – sin 
 Lateral soil pressure, o = KoH
 Resultant force per unit length of wall,
Po = ½ KoH2
The ratio of the horizontal to the vertical stress at any point is defined as the coefficient K.
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 6
 coefficient of active earth pressure, Ka
 Lateral soil pressure, a = KaH
 Resultant force per unit length of wall,
Pa = ½ KaH2
*** Normally (i) and (ii) use for horizontal backfill while (iii) use for sloping backfill.
ii)
i)
iii)
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 7: WORK EXAMPLE 1
Calculate the resultant active thrust on a vertical smooth retaining wall of height 5.4m. The water table is well below the base of the wall.
Soil properties :
 = 30, c = 0,  = 20kN/m3
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 8
Calculate Ka using appropriate equation.
o
Calculate the lateral soil pressure, a = KaH.
Find the resultant active thrust, Pa = ½ KaH2
Determine the point of action at a height of H/3 above the base .
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 9: WORK EXAMPLE 2
Calculate the Rankine active force per unit length of the wall shown below, and also determine the location of the resultant.
5m
γ=15.7kN/m3
Φ’=30
c’=0
Ans : Pa = 65.4kN/m , y = 1.67m
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 10
 coefficient of passive earth pressure, Kp
 Lateral soil pressure, p = KpH
 Resultant force per unit length of wall,
Pp = ½ KpH2
*** Normally (i) and (ii) use for horizontal backfill while (iii) use for sloping backfill.
ii)
i)
iii)
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 11: WORK EXAMPLE 3
For the retaining wall considered below, what is the Rankine passive force per unit length of the wall?
5m
γ=15.7kN/m3
Φ’=30
c’=0
Ans : Pp = 588.75kN/m , y = 1.67m
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 12: Various problem cases
Multi layer
Cohesive soil
Lateral soil pressure,  may increase (for passive) or decrease (for active). The value may be determine using the following equation :
If ground water table encounter in soil
Lateral soil pressure,  will increase. The value may be determine using the following equation :
and
If extra surcharge imposed on top of the soil
Lateral soil pressure,  will increase and its depend to the surcharge value.
Also applicable if imposed by UDL and point load.
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 13: WORK EXAMPLE 4
Determine the active force per unit length of the wall for Rankine state. Also find the location of the resultant. (Das, 2010)
z
GWT
γ = 16 kN/m3
Φ’ = 30
c’ = 0
γsat = 18 kN/m3
Φ’ = 30
c’ = 0
3m
3m
Ans : Pa = 128.394kN/m , y = 1.78m
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 14: WORK EXAMPLE 5
A frictionless retaining wall is shown below, find the passive resistance (Pp) on the backfill, and the location of the resultant passive force.
q=10kN/m2
4m
γ=15kN/m3
Φ=26 
c’=8kN/m2
Ans : Pp = 512kN/m , y = 1.0m
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 15: Coulomb’s lateral earth pressure
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah
He develop the analytical study of lateral earth pressures which he published in 1776 which the theory remains the standard choice of analysis for lateral forces upon structures in soils.
Charles-Augustine de Coulomb (1736-1806)
In Coduto (1998)

## Slide 16
 Assume that failure occurs in the form of a wedge.
 Assume frictions occurs between wall and soil. Coulomb also took into account the inclination of the backfill β, the inclination of the back-wall with respect to the vertical α, and the angle of friction δ between the wall and the soil being retained.
 coefficient of active earth pressure, Ka
 Resultant force per unit length of wall,
Pa = ½ KaH2
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah
Notes: Ka and Kp please refer to textbook

## Slide 17
 coefficient of passive earth pressure, Kp
 Resultant force per unit length of wall,
Pp = ½ KpH2
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 18: WORK EXAMPLE 6
Determine the total active pressure per foot of wall, by Coulomb theory.
α=5 °
Pa
δ=25 °
10m
θ=8°
γ=15kN/m3
φ=30°
δ=25°
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 19: Conclusion
Conclusion #1
  Lateral earth pressure of the soil can be calculated using two methods (Rankine and Coulomb theory).
Conclusion #2
  There are many cases that need to be consider in calculating soil’s lateral earth pressure (cohesion less soil, cohesive soil, horizontal backfill, sloping backfill, multiple layer, additional surcharge, groundwater level).
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah

## Slide 20: Author Information Dr. Amizatulhani Abdullah Dr. Mohd Yuhyi Mohd Tadza Dr. Youventharan Duraisamy Dr. Muzamir Hasan Ir. Azhani Zukri
Lateral Earth Pressure of Soil by Dr. Amizatulhani Abdullah