## Slide 1: GEOTECHNICAL ENGINEERING Slope Stability
by
Dr. Amizatulhani Abdullah Faculty of Civil Engineering ad Earth Resources amizatulhani@ump.edu.my
For updated version, please click on
http://ocw.ump.edu.my

## Slide 2: Chapter description
Aims
  This chapter provides further discussion and explanation related to stability of slope.
Expected Outcomes
  Check and analyze the stability of slopes using various method of analysis and propose the best solution to the problem given.
References
  Das, B.M., “Principles of Geotechnical Engineering, 5th edition”, Thomson Learning (2002).
  Budhu, M., “Soil Mechanics and Foundations, 3rd edition”, John Wiley & Sons (2011).
  Liu, C. & Evett, J.B., “Soils and Foundations, 7th edition”, Prentice Hall (2008).
  Whitlow, R., “Basic Soil Mechanics”, Prentice Hall (2004).
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 3: Content
Introduction of the chapter
Mode of slope failure
Factors in considering method of slope stability analysis
Factor of safety
Infinite slope vs finite slope
Stability of infinite slopes
Conclusion
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 4: Introduction of the chapter
Slope Stability by Dr. Amizatulhani Abdullah
an exposed ground surface that stands at an angle with the horizontal surface.
whenever a mass of soil has an inclined surface, the potential for part of the soil mass to slide from a higher location to a lower one always exists.

## Slide 5: Mode of slope failure
Slope Stability by Dr. Amizatulhani Abdullah
Fall.
Topple.
Slides : Rotational slides, Compound slides, Translational slides (planar).
Spread.
Flows .

## Slide 6
Sliding
Fall
Toppling
Slope Stability by Dr. Amizatulhani Abdullah
Slope failure (Das, 2010)

## Slide 7
Flowing
Spreading
Slope Stability by Dr. Amizatulhani Abdullah
Slope failure (Das, 2010)

## Slide 8: Factors in considering method of slope stability analysis
Types of soil.
Dimension and geometry of the slope (height and gradient).
Gravitational factor.
Pore water pressure.
Tension crack.
Types of analysis.
Vibration or earthquakes.
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 9
Slope Stability by Dr. Amizatulhani Abdullah
Causes of slope failure (Budhu, 2011)

## Slide 10
Slope Stability by Dr. Amizatulhani Abdullah
Causes of slope failure (Budhu, 2011)

## Slide 11
Slope Stability by Dr. Amizatulhani Abdullah
Causes of slope failure (Budhu, 2011)

## Slide 12: Factor of safety
Slope Stability by Dr. Amizatulhani Abdullah
FOS can be expressed in several ways :
General.
With respect to cohesion.
With respect to friction.
FOS = Available Shear Strength
Mobilizied Shear Strength

## Slide 13
where :
Fs = factor of safety with respect to strength
f = average shear strength of the soil
d = average shear stress developed along the potential failure surface
Slope Stability by Dr. Amizatulhani Abdullah
General factor of safety

## Slide 14: Factor of safety with respect to cohesion
Factor of safety with respect to friction
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 15: Infinite slope vs finite slope
Infinite slope
Slope which have great extent with uniform soil conditions at any given depth below the surface.
The soil stratum is not necessary homogenous with depth but the strata of different soils are parallel to the slope surface.
Finite slope
Any slope with limited height.
Eg: slope of embankments, cuts etc.
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 16: Stability of infinite slopes
Slope Stability by Dr. Amizatulhani Abdullah
Stability without seepage

## Slide 17
Stability with seepage
Slope Stability by Dr. Amizatulhani Abdullah
Infinite slope with steady state seepage (Das, 2002)

## Slide 18
An infinite slope is shown below. There is ground water seepage and the ground water table coincides with the ground surface. Determine the factor of safety, Fs.
Work example 1
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 19: Conclusion
Conclusion #1
  There are several types of slope failure mode (fall, topple, sliding, spread, flows).
Conclusion #2
  Factor of safety can be calculated either in general condition, with respect to cohesion and with respect to friction.
Conclusion #3
  In general, slope can be divided into two categories which are infinite slope and finite slope.
Conclusion #4
  The factor of safety of infinite slope is depend on the seepage condition.
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 20: Author Information Dr. Amizatulhani Abdullah Dr. Mohd Yuhyi Mohd Tadza Dr. Youventharan Duraisamy Dr. Muzamir Hasan Ir. Azhani Zukri