## Slide 1: GEOTECHNICAL ENGINEERING Slope Stability
by
Dr. Amizatulhani Abdullah Faculty of Civil Engineering ad Earth Resources amizatulhani@ump.edu.my
For updated version, please click on
http://ocw.ump.edu.my

## Slide 2: Chapter description
Aims
  This chapter provides further discussion and explanation related to stability of slope.
Expected Outcomes
  Check and analyze the stability of slopes using various method of analysis and propose the best solution to the problem given.
References
  Das, B.M., “Principles of Geotechnical Engineering, 5th edition”, Thomson Learning (2002).
  Raj, P.P., “Soil Mechanics & Foundation Engineering”, Prentice Hall (2008).
  Liu, C. & Evett, J.B., “Soils and Foundations, 7th edition”, Prentice Hall (2008).
  Whitlow, R., “Basic Soil Mechanics”, Prentice Hall (2004).
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 3: Content
Stability of finite slopes : plane failure surfaces
Stability of finite slopes : circular failure surfaces
Stability of finite slopes : circular failure surfaces (mass procedure method  = 0)
Stability of finite slopes : circular failure surfaces (mass procedure method  > 0)
Stability of finite slopes : circular failure surfaces (ordinary method of slices)
Stability of finite slopes : circular failure surfaces (Bishop method of slices)
Conclusion
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 4: Stability of finite slopes (plane failure surfaces)
CULMANN’S METHOD
From previous :
The maximum height of the slope can be calculate using the following equation :
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 5
Slope Stability by Dr. Amizatulhani Abdullah
Finite slope analysis by using Culmann’s method (Das, 2002)

## Slide 6: WORK EXAMPLE
A cut is to be made in a soil having =16.5kN/m3, c’=28.8kN/m2 and ’=15. The side of the cut slope will make an angle of 45 with the horizontal. What should be the depth of the cut slope that will have a factor of safety of 3?
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 7: Solution
Ans : 7.04m
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 8: Stability of finite slope (circular failure surfaces)
Slope Stability by Dr. Amizatulhani Abdullah
In this case, the mass of soil above the surface of sliding is taken as a unit. This procedure is useful when the soil that forms the slope is assumed to be homogenous (although this is not the case in most natural slope).
The soil above the surface of sliding is divided into a number of vertical parallel slices. The stability of each slice is calculated separately. This is a versatile technique (no homogeneity, pwp).
MASS PROCEDURE
ORDINARY METHOD OF SLICES

## Slide 9
Toe circle / slope circle
Shallow slope failure
Base failure
Slope Stability by Dr. Amizatulhani Abdullah
Modes of failure of finite slope (Das, 2002)

## Slide 10: Mass procedure (slopes in homogenous clay soil with  = 0)
Slope Stability by Dr. Amizatulhani Abdullah
Soil’s weight, W = cross sectional area x 
Sliding / disturbing moment, Md = Wl
Resisting moment, Mr= cLr where L = r
For equilibrium : Mr = Md
cr2 = Wl1 – Wl2
(Das, 2002)

## Slide 11
The critical failure curve when the ratio of cu to cd is a minimum.
For the case of critical circle, the developed cohesion, cd.
The critical height, Hcr
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 12
Slope Stability by Dr. Amizatulhani Abdullah
Disturbing moment = Wx
Resisting moment = cLr where L = r

## Slide 13
If tension crack occurs;
The slip circle is terminated at the tension crack depth,
If the crack is filled with water, the water pressure should be consider;
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 14
WORK EXAMPLE
A cutting in a saturated clay is inclined at a slope of 1V:1.5H and has a vertical height of 10m. The bulk unit weight of the soil is 18.5kN/m3 and its undrained cohesion is 40kPa. Determine the FOS against immediate shear failure along the slip circle given.
Ignoring the tension crack.
Allowing for tension crack (empty of water).
Allowing for tension crack when full of water.
Ans : 1.44, 1.84, 1.65
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 15
Slope Stability by Dr. Amizatulhani Abdullah
(Whitlow, 2004)

## Slide 16
Slope Stability by Dr. Amizatulhani Abdullah
(Whitlow, 2004)

## Slide 17
Slope Stability by Dr. Amizatulhani Abdullah
(Whitlow, 2004)

## Slide 18
Fellenius (1927( and Taylor (1937) suggested that (for critical circle case) :
where m = Stability number
The corresponding circle that gives the lowest FOS value is called critical circle.
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 19
Slope Stability by Dr. Amizatulhani Abdullah
Definition of parameters for midpoint circle type of falure (Das, 2002)

## Slide 20
WORK EXAMPLE
A cut slope in saturated clay makes an angle of 56 with the horizontal. Determine the maximum depth up to which the cut could be made. Assume that the critical surface for sliding is circularly cylindrical. What will be the nature of the critical circle?
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 21: Mass procedure (slopes in homogenous clay soil with  > 0)
TAYLOR’S STABILITY CHART
Taylor proposed stability coefficients for the analysis of homogeneous slopes.
stability number, m can be obtain from stability charts – Taylor’s stability number.
Slope Stability Dr. Amizatulhani Abdullah

## Slide 22
Slope Stability by Dr. Amizatulhani Abdullah
Taylor’s stability number (Das, 2002)

## Slide 23: WORK EXAMPLE
Find the critical height of a slope with  = 45 to be constructed with a soil having ’ = 20 and c’ = 15kN/m2. The unit weight of the compacted soil will be 17kN/m3.
Ans : 14.706m
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 24: WORK EXAMPLE
A slope is shown in figure below. Determine the factor of safety with respect to strength.
You might need to use graph papers
Ans : 1.73
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 25
Assume d.
Find m by using Taylor’s stability number chart.
Calculate cd.
Determine Fc and F. Both value must be the same. If not, make another trial by assume new value of d.
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 26: Stability of finite slope (ordinary method of slices)
Slope Stability by Dr. Amizatulhani Abdullah
ORDINARY METHOD OF SLICES
The soil above the surface of sliding is divided into a number of vertical parallel slices. The stability of each slice is calculated separately. This is a versatile technique (no homogeneity, pwp).

## Slide 27
Slope Stability by Dr. Amizatulhani Abdullah
Stability analysis by ordinary method of slices (Das, 2002)

## Slide 28
Procedure
Draw to scale a cross section of the slope.
A trial curved surface along which sliding is assumed to take place is drawn.
The trial surface is normally approximately circular.
Soil between the trial surface and the slope is then divided into a number of vertical slices of equal width.
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 29
Weight of soil within each slice = Slice volume x Soil unit weight
Noted as W.
Can be resolved into two component ;
i) component of W normal to the base, Wn and
ii) component of W parallel to the base, Wp
It is the parallel component that tends to cause sliding.
Resisting to sliding is afforded by the soil’s cohesion and internal friction.
Cohesion force = Soil cohesion x Length of the slice
Friction force = Wn x Friction coefficient, tan 
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 30
Apply value into formula
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 31: WORK EXAMPLE
Find the factor of safety against sliding for the trial slip surface given. Use ordinary method of slices.
Ans : 1.55
Slope Stability by Dr. Amizatulhani Abdullah
(Das, 2002)

## Slide 32
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 33: Stability of finite slope (Bishop method of slices)
Slope Stability by Dr. Amizatulhani Abdullah
BISHOP METHOD OF SLICES
Bishop proposes a more refined solution to previous method where the effect of forces on the sides of each slice are accounted.
Procedure
Trial and error to find the value of Fs
where :

## Slide 34
where :
Slope Stability by Dr. Amizatulhani Abdullah
Bishop’s simplified method of slices (Das, 2002)

## Slide 35
Several number of failure surface must be investigated so that the critical surface(yields the lowest FOS value) can be found.
This method gives satisfactory results in most cases when incorporated into computer programs.
Widely used.
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 36: Conclusion
Conclusion #1
  There are various method that can be use to analyze finite slope stability and it depends to the types of failure surface (either plane or circular).
Conclusion #2
  For finite slope with circular failure surface, the analysis can be further divided into following: 1) Mass procedure ( = 0 or  > 0) 3) Method of slices (ordinary or Bishop)
Slope Stability by Dr. Amizatulhani Abdullah

## Slide 37: Author Information Dr. Amizatulhani Abdullah Dr. Mohd Yuhyi Mohd Tadza Dr. Youventharan Duraisamy Dr. Muzamir Hasan Ir. Azhani Zukri