## Slide 1: GEOTECHNICAL ENGINEERING Shear Strength of Soil
by
Dr. Amizatulhani Abdullah Faculty of Civil Engineering ad Earth Resources amizatulhani@ump.edu.my
For updated version, please click on
http://ocw.ump.edu.my

## Slide 2: Chapter description
Aims
  This chapter provides further discussion and explanation related to shear strength of soil.
Expected Outcomes
  Understand the concept of Mohr Coulomb shear strength.
References
  Das, B.M., “Principles of Geotechnical Engineering, 5th edition”, Thomson Learning (2002).
  Coduto, D.P., “Geotechnical Engineering Principles and Practices”, Prentice Hall (1998).
  Liu, C. & Evett, J.B., “Soils and Foundations, 7th edition”, Prentice Hall (2008).
  Whitlow, R., “Basic Soil Mechanics”, Prentice Hall (2004).
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 3: Content
Introduction
Mohr-Coulomb failure criterion
Laboratory test to determine shear strength parameters ; Direct shear test
Conclusion
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 4: Introduction
The shear strength of a soil mass is the internal resistance per unit area that the soil mass can offer to resist failure and sliding along any plane inside it.
The capability of the following comes from the soil shear strength :
 Support loading from structure
 Support its own overburden
 Sustain slope in equilibrium
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 5
Soil derives its shear strength from two sources:
  Cohesion between particles (stress independent component) - c
    Cementation between particle grains.
    Electrostatic attraction between clay particles.
    Predominant in clayey soils.
  Frictional resistance between particles (stress dependent component) - 
    Strength gained from internal frictional resistance (interlocking action among soil particles).
    Predominant in granular soils.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 6: COHESION
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 7: INTERNAL FRICTION
Shear strength is not a unique property of a soil but depends on many factors.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 8
Failure happens if the shear stress along the failure surface reaches the soil’s shear strength.
Soil generally fail in shear.
failure surface
mobilised shear resistance
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 9

f

At failure, shear stress along the failure surface () reaches the shear strength (f).
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 10: Mohr Coulomb failure criterion
Shear Strength of Soil by Dr. Amizatulhani Abdullah
Mohr presented in 1900 a theory of rupture of materials, that was the result of a combination of both normal and shear stresses. The shear stress at failure is thus,
Charles Mohr
Charles Coulomb
Coduto (1998)

## Slide 11
The limiting shear stress (soil strength) is given by :
 = c +  tan 
where
c = cohesion
 = angle of internal friction
t
sn
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 12
Shear Stress, 
Normal Stress,  = 
C
 = 
Gradient of the line
Interception of y-axis
Mohr-Coulomb envelope
f is the maximum shear stress the soil can take without failure, under normal stress of .
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 13
X
Y
Soil elements at different locations
X
Y
X
Y
~ failure
~ stable


Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 14
Y
Initially, Mohr circle is a point
c
c
c

c+

The soil element does not fail if the Mohr circle is contained within the envelope.
GL
c
As loading progresses, Mohr circle becomes larger…
.. and finally failure occurs when Mohr circle touches the envelope.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 15
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 16
Y
c
c
c

GL
c+
90+

45 + /2
Failure plane oriented at 45 + /2 to horizontal
45 + /2
Y
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 17: EFFECTIVE STRESS FAILURE CRITERION
If the soil is at failure the effective stress failure criterion will always be satisfied.
Soil behavior is controlled by effective stresses, and the effective strength parameters are the fundamental strength parameters. But they are not necessarily soil constants.
c’ and f’ are known as the effective (or drained) strength parameters.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 18: TOTAL STRESS FAILURE CRITERION
If the soil is taken to failure at constant volume (undrained) then the failure criterion can be written in terms of total stress as
cu and fu are known as the undrained strength parameters.
These parameters are not soil constants, they depend strongly on the moisture content of the soil.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 19: Laboratory test to determine shear strength parameters
Direct Shear Test
Triaxial Test
Vane Shear Test
Unconfined Compression Test
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 20: DIRECT SHEAR TEST
Motor drive
Load cell to measure shear force
Normal load
Rollers
Soil
Porous plates
Top platen
Measure relative horizontal displacement, dx and vertical displacement of top platen, dy
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 21: TEST PROCEDURE
Soil specimen (round or square) is placed in a relatively flat box and subjected to a vertical load.
The box consists 2 parts (upper and lower).
If 1 part of the box held while another one being pushed, the specimen will experience shear failure along the horizontal surface.
Vertical load and shear force that induced the failure of the specimen is recorded.
The failed sample is discarded and another sample is placed in the box.
Experiment is repeated several times.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 22: TYPICAL RESULT
Normal load increasing
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 23
After failure, stress is attained, the resisting shear stress gradually decreases as shear displacement increases until it finally reaches a constant value called the ultimate shear strength.
In dense sand, the resisting shear stress increases with shear displacement until it reaches a failure stress f.
f is called the peak shear strength.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 24
Draw suitable axes (x and y) on a graph paper. The same scale should be used for both axes.
Using the axes, plot normal stress vs shear stress.
Draw a best fit line connecting all the points plotted.
Based on the plot, the following parameters obtained :
Cohesion, c – interception at y-axis.
Angle of internal friction,  = gradient of the straight line.
DATA ANALYSIS
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 25
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 26
ADVANTAGES
DISADVANTAGES
Most easiest and quickest test.
Large samples may be tested in large shear boxes. Small samples may give misleading results due to imperfections (fractures and fissures) or the lack of them.
Samples may be sheared along predetermined planes. This is useful when the shear strengths along fissures or other selected planes are required.
The shear failure is forced to occur along or across a predetermined plane which is not necessarily the weakest plane of the soil specimen tested
Non-uniform deformations and stresses in the specimen. The stress-strain behavior cannot be determined. The estimated stresses may not be those acting on the shear plane.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 27
In practice shear box tests are used to get quick and crude estimates of failure parameters.
Since development of the much better triaxial test, the used of the direct shear test has decreased.
APPLICATION
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 28
WORK EXAMPLE
A direct shear test conducted on a soil sample yielded the following results:
Normal Stress,  (psi) | Max. Shear Stress, S (psi)
10.0 | 6.5
25.0 | 11.0
40.0 | 17.5
Determine shear strength parameters of the soil.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 29
ANSWER :
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 30: Conclusion
Conclusion #1
  Shear strength of soil is govern by two parameters which are the cohesion and the angle of internal friction.
Conclusion #2
  Cohesion value can be obtained at the interception of shear stress axis while angle of internal friction is depends on the gradient of the Mohr Coulomb failure envelope.
Conclusion #3
  There are several tests that can be use to determine shear strength parameters of soil (direct shear test, triaxial test, unconfined compression test and vane shear test).
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 31: Author Information Dr. Amizatulhani Abdullah Dr. Mohd Yuhyi Mohd Tadza Dr. Youventharan Duraisamy Dr. Muzamir Hasan Ir. Azhani Zukri