## Slide 1: GEOTECHNICAL ENGINEERING Shear Strength of Soil
by
Dr. Amizatulhani Abdullah Faculty of Civil Engineering ad Earth Resources amizatulhani@ump.edu.my
For updated version, please click on
http://ocw.ump.edu.my

## Slide 2: Chapter description
Aims
  This chapter provides further discussion and explanation related to shear strength of soil.
Expected Outcomes
  Apply various method of laboratory test to evaluate shear strength of soil.
References
  Das, B.M., “Principles of Geotechnical Engineering, 5th edition”, Thomson Learning (2002).
  Budhu, M., “Soil Mechanics and Foundations, 3rd edition”, John Wiley and Sons (2010).
  Liu, C. & Evett, J.B., “Soils and Foundations, 7th edition”, Prentice Hall (2008).
  Whitlow, R., “Basic Soil Mechanics”, Prentice Hall (2004).
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 3: Content
Laboratory test to determine shear strength parameters ; Triaxial test, vane shear test, unconfined compression test
Stress path
Sensitivity and thixotrophy
Conclusion
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 4: TRIAXIAL TEST
Cell pressure
Pore pressure and volume change
Rubber membrane
Cell water
O-ring seals
Porous filter disc
Confining cylinder
Deviator load
Soil
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 5: TEST PROCEDURE
Cylindrical soil specimen (wrapped in a rubber membrane) is subjected to a vertical load.
This test require the present of the confining / lateral pressure.
Specific value of confining pressure is achieved by introducing water or compressed air into the chamber to surround the soil specimen.
The vertical load is applied and steadily increased until the specimen fails.
The vertical load and the lateral pressure that cause the specimen failed is recorded.
The test is repeated several times.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 6: TYPICAL RESULT

e
Increasing cell pressure
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 7
sr
sr = Radial stress (cell pressure)
sa = Axial stress
F = Deviator load
sr
From equilibrium we have,
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 8
F/A is known as the deviator stress, and is given the symbol q
where
1 = axial pressure / major principal stress
3 = lateral pressure / minor principal stress
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 9
By plotting 1 and 3 in a graph, we can determine :
Cohesion, c
Angle of internal friction, 
HOW ?
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 10
Draw suitable axes (x and y) in a graph paper. The same scale should be used for both axes.
Using 1 and 3 values obtained from several triaxial tests, draw a semicircle.
Draw a straight tangent line (touch both semicircles, if possible) to the semicircles.
The straight line is called the Strength Envelope @ Failure Envelope @ Mohr’s envelope.
c value obtained from the y-axis while  value obtained from the gradient of the strength envelope.
Shear Strength of Soil by Dr. Amizatulhani Abdullah
DATA ANALYSIS

## Slide 11
t
s
s1
s3
c
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 12
TYPES OF TRIAXIAL TEST
There are many test variations. Those used most in practice are:
UU (unconsolidated undrained) test.
Cell / lateral pressure is applied without allowing drainage. Then keeping cell pressure constant, increase deviator / axial load to failure without drainage.
CU (isotropically consolidated undrained) test.
Drainage allowed during cell pressure application. Then without allowing further drainage increase deviator / axial load, keeping cell pressure constant as for UU test.
CD (isotropically consolidated drained) test.
Similar to CU except that as deviator stress is increased drainage is permitted.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 13
Test type | Step 1 | Step 2
Consolidated drained, CD | Apply chamber pressure, 3. Allow complete drainage, so pore water pressure (u = u0) developed is zero | Apply axial stress, , slowly. Allow drainage, so pore water pressure (u = ud) developed through application of  is zero. At failure,  = f ; total pore water pressure, uf = ua + ud = 0
Consolidated undrained, CU | Apply chamber pressure, 3. Allow complete drainage, so pore water pressure (u = u0) developed is zero | Apply axial stress, . Do not allow drainage (u = ud  0). At failure,  = f ; pore water pressure, u = uf = ua + ud = 0 + ud(f)
Unconsolidated undrained, UU | Apply chamber pressure, 3. Do not allow drainage, so pore water pressure (u = u0) developed through application of 3 is not zero | Apply axial stress, . Do not allow drainage (u = ud  0). At failure,  = f ; pore water pressure, u = uf = ua + ud(f)
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 14
ADVANTAGES
Specimens are subjected to (approximately) uniform stresses and strains.
The complete stress-strain-strength behavior can be investigated.
Drained and undrained tests can be performed.
Pore water pressures can be measured in undrained tests, allowing effective stresses to be determined.
Different combinations of cell pressure and axial stress can be applied.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 15
WORK EXAMPLE
The results of a trixial test are as follows :
No of test | Chamber confining pressure, kN/m2 | Deviator stress at failure, kN/m2
1 | 100 | 210
2 | 200 | 438
3 | 300 | 644
Draw the shear strength envelope and determine the shear strength parameters of the soil.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 16
Solution :
1. Complete the following table.
Using the graph paper (same scale on both axis), draw the mohr envelope and sketch the tangent line.
Check the interception on y-axis and the gradient of the line.
No of test | 3, kN/m2 | , kN/m2 | 1, kN/m2
1 | 100 | 210 | 
2 | 200 | 438 | 
3 | 300 | 644 | 
Hint : 1 = 3 + 
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 17: UNCONFINED COMPRESSION TEST
A special type of UU test (triaxial test) that is commonly used for clay specimen.
σ3 = 0
Axial load rapidly applied to the specimens to cause failure.
At failure the total minor principal stress is zero and total major stress is σ1
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 18: TYPICAL RESULT
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 19: General Relationship of Consistency and Unconfined Compression Strength of Clays
Consistency | qu | 
 | ton/ft2 | kN/m2
Very soft | 0 – 0.25 | 0 – 24
Soft | 0.25 – 0.5 | 24 – 48
Medium | 0.5 – 1 | 48 – 96
Stiff | 1 – 2 | 96 – 192
Very stiff | 2 – 4 | 192 – 383
Hard |  4 |  383
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 20: VANE SHEAR TEST
Vane shear apparatus : consists of four thin, equal sized steel plates welded to a steel torque rod.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 21
Shear Strength of Soil by Dr. Amizatulhani Abdullah
Vane shear tester (Budhu, 2010)

## Slide 22: TEST PROCEDURE
This test is used to determine shear strength of cohesive soils.
Normally done in-situ on a soft clayey soil (cohesive soil).
The vane is pushed into the soil.
Torque,T is applied at the top of the torque rod to rotate the vane at a uniform speed.
A cylinder of soil (height h & diameter d) will resist the torque until the soil fails.
where  = coefficient of shear strength mobilization at the end of soil cylinder.
= 1/2 @ 2/3 @ 3/5
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 23
Bjerrum (1974) showed that as the plasticity of soils increases, cu obtained from VST may give results that are unsafe for foundation design. Therefore, he suggested that some correction should be made :
Morris and Williams (1994) gave the correlations of  as :
cu (design) = cu (VST)
where  = correction factor = 1.7 - 0.54log(PI)
 = 1.18e-0.08(PI) + 0.57 (for PI  5)
 = 7.01e-0.08(LL) + 0.57 (for LL  20)
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 24
1. Ring shear test
2. Cone penetration test
(ASTM D3441 and D5778)
3. Standard penetration test
(ASTM D1586)
4. Penetrometer test
Field test
Laboratory test
OTHER METHOD TO
DETERMINE SOIL’S SHEAR STRENGTH
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 25: Stress path
A convenient way of plotting triaxial test data is through diagrams called stress paths.
Stress path = line that connects a series of point, each of which represents a successive stress state experienced by a soil specimen during the process of a test
Lamb (1964) suggested a new coordinate system of p’ versus q’ where,
Stress path = diagrams/graphs of stress changes
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 26
Stress path in / space
Stress path in 1/3 space
Stress path in t’/s’ space
Stress path in q’/p’ space
Advance level
TYPES OF STRESS PATH
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 27
Results of triaxial tests can be represented by stress path.
Consider a normally consolidated clay subjected to an isotropically consolidated-drained triaxial test.
At the beginning of the test, the deviatoric stress σ1’ = σ3’ = σ3, so,
Shear Strength of Soil by Dr. Amizatulhani Abdullah
Stress path for a consolidated drained triaxial test on a normally consolidated clay (Das, 2002)

## Slide 28
and the p’ and q’ will plot as point I (in previous figure). As the load is increased, the deviatoric stress σ1’ = σ3’ + <σd and σ3’ = σ3, and the Mohr circle A corresponds to that state.
These two equations plot as point D’ at the top of the Mohr circle A.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 29
Each successive plot of p’ and q’ will continue this straight line that is at an angle of 45° with respect to the p’ axis.
Eventually we will reach the point D on the Mohr circle B, and the sample fails (it has reached the modified failure envelope).
From this, q ' = p ' tanα
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 30: Sensitivity & thixotrophy
For naturally deposited clay soils, unconfined compression strength is reduced greatly when the soils are tested after remolding without any change in moisture content.
This property is called sensitivity.
The loss of strength of clay soils due to remolding is primarily due to the destruction of the clay particle structure that was developed during the original process of sedimentation.
If, however, after remolding a soil specimen is kept in an undisturbed state (that is, without any change of moisture content), it will continue to gain strength with time.
This phenomenon is referred to as thixotropy.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 31
Sensitivity = the reduction in unconfined compression strength of clay soils due to remolding although no changes in the moisture content
Degree of sensitivity, St =
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 32
may range from 1 to 8 or might be reached as high as 80 (flocculent marine clay deposits)
1
8
16
32
64
2
4
Slightly sensitive
Medium sensitive
Very sensitive
Slightly quick
Medium quick
Very quick
Extra quick
Sensitivity, St (log scale)
There are some clays that turn to viscous fluids upon remolding. These are found mostly in the previously glaciated areas of North America and Scandanavia.
These clays are referred to as “quic” clays.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 33
Thixotrophy = is a condition whereby a soil specimen which is kept in undisturbed condition (after remolding) will experienced a continuous increased in strength with time.
The loss of strength is gradually regained with time when the materials are allowed to rest.
However most soils are partially thixotropic (part of the strength loss caused by remolding is never regained with time)
The soils strength will never achieved the initial strength although the specimen were prepared undisturbed.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 34: Conclusion
Conclusion #1
  There are several tests that can be use to determine shear strength parameters of soil (direct shear test, triaxial test, unconfined compression test and vane shear test).
Conclusion #2 (important terminology)
  Stress path is a line that connects a series of point, each of which represents a successive stress state experienced by a soil specimen during the process of a test.
  Sensitivity is the reduction in unconfined compression strength of clay due to remolding although there is no changes in moisture content.
  Thixotrophy is a condition whereby a soil specimen which is kept in undisturbed condition (after remolding) will experienced a continuous increased in strength with time.
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 35: Author Information Dr. Amizatulhani Abdullah Dr. Mohd Yuhyi Mohd Tadza Dr. Youventharan Duraisamy Dr. Muzamir Hasan Ir. Azhani Zukri