## Slide 1: GEOTECHNICAL ENGINEERING Shear Strength of Soil (Learning activities)
by
Dr. Amizatulhani Abdullah Faculty of Civil Engineering ad Earth Resources amizatulhani@ump.edu.my
For updated version, please click on
http://ocw.ump.edu.my

## Slide 2: Reference
  1) Das, B.M., “Principles of Geotechnical Engineering, 5th edition”, Thomson Learning (2002).
Shear Strength of Soil by Dr. Amizatulhani Abdullah

## Slide 3
Shear Strength of Soil by Dr. Amizatulhani Abdullah
A direct shear test was conducted on a specimen of dry sand with a normal stress of 200kN/m2. Failure occurred at a shear stress of 175kN/m2. The size of the specimen test was 75mm x 75mm x 30mm (height). Determine the angle of friction, . For a normal stress of 150k/m2, what shear force would be required to cause failure in the specimen?

## Slide 4
Shear Strength of Soil by Dr. Amizatulhani Abdullah
Following are the results of four drained direct shear tests on a normally consolidated clay:
Size of specimen = 60mm x 60mm
Height of specimen = 30mm
Test no. | Normal force (N) | Shear force at failure (N)
1 | 200 | 155
2 | 300 | 230
3 | 400 | 310
4 | 500 | 385

## Slide 5
Shear Strength of Soil by Dr. Amizatulhani Abdullah
The shear strength of a normally consolidated clay can be given by the equation f =  tan 31. A consolidated undrained test was conducted on the clay. Following are the results of the test:
Chamber confining pressure = 112kN/m2
Deviator stress at failure = 100kN/m2
Determine:
The consolidated undrained friction angle, 
The pore water pressure developed in the clay specimen at failure.

## Slide 6
Shear Strength of Soil by Dr. Amizatulhani Abdullah
The following are the results of a consolidated undrained triaxial test in a clay. Draw the total stress Mohr’s circles and determine the shear strength parameters for consolidated undrained conditions
Test no. | 3 (kN/m2) | 1 at failure (kN/m2)
1 | 192 | 375
2 | 384 | 636

## Slide 7: Author Information Dr. Amizatulhani Abdullah Dr. Mohd Yuhyi Mohd Tadza Dr. Youventharan Duraisamy Dr. Muzamir Hasan Ir. Azhani Zukri