## Slide 1: GEOTECHNICAL ENGINEERING Soil Compression, Consolidation and Settlement
by
Dr. Amizatulhani Abdullah Faculty of Civil Engineering ad Earth Resources amizatulhani@ump.edu.my
For updated version, please click on
http://ocw.ump.edu.my

## Slide 2: Chapter description
Aims
  This chapter provides further discussion and explanation related to soil consolidation and settlement.
Expected Outcomes
  Understand the theory of consolidation.
References
  Das, B.M., “Principles of Geotechnical Engineering, 5th edition”, Thomson Learning (2002).
  Raj, P.P., “Soil Mechanics & Foundation Engineering”, Prentice Hall (2008).
  Liu, C. & Evett, J.B., “Soils and Foundations, 7th edition”, Prentice Hall (2008).
  Whitlow, R., “Basic Soil Mechanics”, Prentice Hall (2004).
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 3: Content
Introduction
Types of settlement
Immediate settlement
Fundamental of consolidation (piston-spring model)
One dimensional consolidation test
Conclusion
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 4: Introduction
Problems due to excessive settlement
1) Aesthetic view : the aesthetical value of the structure might spoiled due to presence of cracks or tilt of the structure caused by settlement.
2) Structure damage : the damages of some structure such as buildings and also utilities drains, pumps or electrical lines.
3) Structure failure : cause a structure to fail structurally and collapse.
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 5: Types of settlement
Settlement
Immediate settlement
Primary consolidation settlement
Secondary consolidation settlement
+
+
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 6: Immediate settlement
Caused by the elastic deformation of dry soil and of moist and saturated soils without any change in the moisture content in the soil.
Usually occurred immediately after load is imposed.
Completed quickly.
Constitutes a relatively small amount of total settlement.
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 7
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah
(Das, 2002)

## Slide 8
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah
(Das, 2002)

## Slide 9
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah
(Das, 2002)

## Slide 10: Example
Estimate the immediate settlement of a column footing 1.5m in diameter that is constructed on an unsaturated clay layer, given that the total carried by the column footing = 150kN, Es = 7000kN/m2 and s = 0.25. Assume the footing to be rigid.
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 11: Fundamental of consolidation (piston-spring model)
in this analogy spring act as the soil skeleton.
while water act as the water in the soil.
the valve act as the void in the soil which effect the permeability of the soil.
Spring
Valve
Water
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 12
Condition 1
(if load is imposed while the valve is closed)
Valve closed
Spring will not move due to the incompressibility of water.
Therefore, no load transferred to spring because it was all carried by water.
This also called the undrained condition in soil.
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 13
Condition 2
(if load is imposed while the valve is opened)
Valve opened
Water were forced to flow out through the valve.
The flow rate depend to the diameter of the hole/valve.
Some of the load carried by water while some were transferred to the spring.
The load increment to the spring depend to the decrease of pore water pressure.
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 14
After all the water extruded, the load were totally carried by spring.
Deformation continue to occur until the spring reach the final condition.
This condition shows the drained condition in soil.
No more water inside
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 15
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah
Variation of total stress, pore water pressure and effective stress in a clay layer drained at top and bottom as the result of an added stress
(Das, 2002)

## Slide 16: At t=0
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah
(Das, 2002)

## Slide 17: At 0  t  
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah
(Das, 2002)

## Slide 18
At t = 
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah
(Das, 2002)

## Slide 19: One dimensional consolidation test
Oedometer test
Used to determine the compressibility characteristics of a saturated undisturbed or remolded soil.
Sample were collected from site.
Sample is placed in a metal ring.
Porous disk is placed above and beneath the sample (to allow water to flow vertically into and out of the soil sample).
The sample is immersed in water.
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 20
Porous stone
Porous stone
Soil specimen
Specimen ring
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah
Schematic diagram of a consolidometer (Das, 2002)

## Slide 21
A specific load pressure is applied to the upper disk (the sample is compressed and deformation is measured by a dial gauge).
Dial readings and corresponding time observations are made and recorded until deformation has nearly ceased (normally 24 hour).
Graph is plotted.
The procedure will be repeated with the applied pressure doubled from the previous.
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 22: Typical result of an oedometer test
Time-deformation plot : graph with time along the abscissa (logarithmic scale) and dial readings along the ordinate (arithmetic scale).
Stage 1
Stage 2
Stage 3
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 23
Pressure-void Ratio Curves : graph with pressure along the abscissa (logarithmic scale) and void ratio along the ordinate (arithmetic scale).
Compression curve
Recompression curve
Rebound curve
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 24: Conclusion
Conclusion #1
  Settlement of soil can be divided into three categories (immediate settlement, primary consolidation settlement, secondary consolidation settlement).
Conclusion #2
  Fundamental on consolidation can be further explain using piston spring model.
Conclusion #3
  One dimensional test or also known as oedometer test is a laboratory test to measure compressibility characteristics of soil.
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 25: Author Information Dr. Amizatulhani Abdullah Dr. Mohd Yuhyi Mohd Tadza Dr. Youventharan Duraisamy Dr. Muzamir Hasan Ir. Azhani Zukri