## Slide 1: GEOTECHNICAL ENGINEERING Soil Compression, Consolidation and Settlement (Learning activities)
by
Dr. Amizatulhani Abdullah Faculty of Civil Engineering ad Earth Resources amizatulhani@ump.edu.my
For updated version, please click on
http://ocw.ump.edu.my

## Slide 2: Reference
  1) Das, B.M., “Principles of Geotechnical Engineering, 5th edition”, Thomson Learning (2002).
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 3
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah
Following are the results of a consolidation test.
Plot the e log  curve
Using Casagrande’s method, determine the preconsolidation pressure
Calculate the compression index Cc from the laboratory e log  curve
e | Pressure,  (kN/m2)
1.21 | 25
1.195 | 50
1.15 | 100
1.06 | 200
0.98 | 400
0.925 | 500

## Slide 4
A soil profile is shown in Figure 1. The uniformly distributed load on the ground surface is . Estimate the primary settlement of the normally consolidated clay layer, given that:
H1=2.5m, H2=2.5m, H3=3m
For sand, e=0.64, Gs=2.65
For clay, e=0.9, Gs=2.75, LL=55
=100kN/m2
Soil Compression, Consolidation and Settlement by Dr. Amizatulhani Abdullah

## Slide 5: Author Information Dr. Amizatulhani Abdullah Dr. Mohd Yuhyi Mohd Tadza Dr. Youventharan Duraisamy Dr. Muzamir Hasan Ir. Azhani Zukri