## Slide 1: BSB3503 - Biomanufacturing CHAPTER 6 Good Manufacturing Practices (General)
Author: Nurul Azyyati Sabri
Co-Author / Editor: Rama Yusvana Faculty Industrial Sciences & Technology yusvana@ump.edu.my

## Slide 2: Learning Outcomes
Understand GMP concept, the principles as well as the practice.
Understand the importance of GMP

## Slide 3: 1. “Writing detailed step-by-step procedures that provide a roadmap for controlled and consistent performance”
Ten (10) Principles of GMP

## Slide 4: 2. “Carefully following written procedures to prevent contamination, mixups and errors”
Ten (10) Principles of GMP

## Slide 5
  Operations performed within specifically defined areas
  Separate or defined areas to prevent contamination or mixups as follows:
Areas for receipt, identification, storage
Areas for folding rejected components;
Storage of released components;

## Slide 6
“Storage of in-process materials”
“Manufacturing and processing operations”
“Packaging and labeling operations”
“Quarantine storage before release of drug products”
“Storage of drug products after release”
“Control and laboratory operations”
“Aseptic processing, which includes anything as appropriate”
  In order to prevent contamination or mixups the areas must also include as follows:

## Slide 7: 3. “Promptly and accurately documenting work for compliance and traceability”
Ten (10) Principles of GMP
Note: Refer to GMP Chapter on Documentation

## Slide 8: 4. “Proving that systems do what they are designed to do by validation work”
Ten (10) Principles of GMP
Note: Refer to GMP Chapter on Validation

## Slide 9: 5. “Integrating productivity, product quality, and employee safety into the design and construction of facilities and equipment”
Ten (10) Principles of GMP

## Slide 10
Paragraph 42 of CFR 211 Design and Construction of features:
§ 211.42 Design and construction features.
  (a) “Any building or buildings used in the manufacture, processing, packing, or holding of a drug product shall be of suitable size, construction, and location to facilitate cleaning, maintenance, and proper operations”.

## Slide 11
  (b) “Any such building shall have adequate space for the orderly placement of equipment and materials to prevent mixups between different components of drug product, containers, closures (lids), labeling, in-process materials, or drug products, and to prevent contamination”.
  (c) ”The flow of components, drug product containers, closures, labeling, in-process materials, and drug products through the building or buildings shall be designed to prevent contamination”.

## Slide 12: 6. Properly maintain facilities and equipment
Ten (10) Principles of GMP

## Slide 13
Paragraph 44 of CFR 211 addresses lighting issues and states:
§ 211.44 Lighting: Adequate lighting shall be provided in all areas
  (d) “Operations relating to the manufacture, processing, and packing of penicillin shall be performed in facilities separate from those used for other drug products for human use”.

## Slide 14
Paragraph 46 of CFR 211 addresses ventilation systems and states:
§ 211.46 Ventilation, air filtration, air heating and cooling.
(a) “Adequate ventilation shall be provided”.
(b) “Equipment for adequate control over air pressure, microorganisms, dust, humidity, and temperature shall be provided when appropriate for the manufacture, processing, packing, or holding of a drug product”.
  (d) “Operations relating to the manufacture, processing, and packing of penicillin shall be performed in facilities separate from those used for other drug products for human use”.

## Slide 15
(c) “Air filtration systems, including prefilters and particulate matter air filters, shall be used when appropriate on air supplies to production areas. If air is recirculated to production areas, measures shall be taken to control recirculation of dust from production”.
§ 211.46 Ventilation, air filtration, air heating and cooling.

## Slide 16
“In areas where air contamination occurs during production, there shall be adequate exhaust systems or other systems adequate to control contaminants”.
§ 211.46 Ventilation, air filtration, air heating and cooling.

## Slide 17
(d) “Air-handling systems for the manufacture, processing, and packing of penicillin shall be completely separate from those for other drug products for human use”.
§ 211.46 Ventilation, air filtration, air heating and cooling.

## Slide 18
The regulations dealing with equipment requirements:
§ 211.63 Equipment design, size, and location.
  “Equipment used in the manufacture, processing, packing, or holding of a drug product shall be of appropriate design, adequate size, and suitably located to facilitate operations for its intended use and for its cleaning and maintenance”.

## Slide 19
§ 211.65 Equipment construction.
  (a) “Equipment shall be constructed so that surfaces that contact components, inprocess materials, or drug products shall not be reactive, additive, or absorptive so as to alter the safety, identity, strength, quality, or purity of the drug product beyond the official or other established requirements”.

## Slide 20
§ 211.65 Equipment construction.
  (b) “Any substances required for equipment operation, such as lubricants or coolants, shall NOT come into contact with components, containers, closures, in-process materials, or drug products so as to alter the safety, identity, strength, quality, or purity of the drug product beyond the official or other established requirements”.

## Slide 21: 7. Clearly defining, developing and demonstrating job competence
Ten (10) Principles of GMP

## Slide 22: 8. Protecting products against contamination by making cleanliness a daily habit
Ten (10) Principles of GMP
  (d) “Operations relating to the manufacture, processing, and packing of penicillin shall be performed in facilities separate from those used for other drug products for human use”.

## Slide 23
Paragraph 46 of CFR 211 addresses ventilation systems and states:
§ 211.46 Ventilation, air filtration, air heating and cooling.
(a) “Adequate ventilation shall be provided”.
(b) “Equipment for adequate control over air pressure, microorganisms, dust, humidity, and temperature shall be provided when appropriate for the manufacture, processing, packing, or holding of a drug product”.

## Slide 24: 9. “Building quality into products by systematically controlling our components and product related processes such as manufacturing, packaging and Labelling, testing, distribution and marketing”
Ten (10) Principles of GMP

## Slide 25: 10. Conducting planned and periodic audits for compliance and performance
Ten (10) Principles of GMP

## Slide 26: Definition of GMP
WHO defines Good Manufacturing Practices (GMP) as “that part of quality assurance which ensures that products are consistently produced and controlled to the quality standards appropriate to their intended use and as required by the marketing authorization”

## Slide 27
In GMP quality is built into a product.
Quality Assurance the product meets the final specifications.

## Slide 28
  “defined manufacturing process”
  “validated critical manufacturing steps”
  “suitable premises, storage, transport”
  “qualified and trained production and quality control personnel”
GMP covers all aspects of the manufacturing process:

## Slide 29
  “Adequate laboratory facilities”
  “approved written procedures and instructions”
  “records to show all steps of defined procedures taken”
  “full traceability of a product through batch processing records and distribution records”
  “systems for recall and investigation of complaints”.
GMP covers all aspects of the manufacturing process:

## Slide 30
The pharmaceutical industry needs to produce safe products.
Challenges to plan, design, construct, validate manufacturing facilities.
Due to increased demand for pharmaceuticals.

## Slide 31
Combined with growing productivity in research and development.
Guidelines were developed by the pharma-focused regulatory bodies.

## Slide 32
The modern pharmaceutical industry took shape in the mid-20th century.
International pharmaceutical organizations were forming to manufacture drug products,.

## Slide 33
Today, several firms have over 5% share and Pfizer acquired Warner-Lambert and Pharmacia, has over 11% worldwide market share.

## Slide 34
Manufacturing requirements increasingly complex.
The pharmaceutical industry is strongly regulated.

## Slide 35
The primary health care regulators (FDA, Medicines and Healthcare products Regulatory Agency (MHRA) and WHO) are cooperating to rationalize rules and improve risks assessment and safety profiles

## Slide 36
There are many ways this is controlled:
controlling facility and its systems
controlling raw materials,
controlling production at all stages,
controlling the testing of the product,
controlling the identity of materials
controlling the storage, etc.

## Slide 37
All of these controls must follow prescribed, formal, approved procedures, written as protocols, SOPs or Master Formulae.

## Slide 38: GMP Family
Other good-practice systems, along the same lines as GMP, exist:
“Good laboratory practice” (GLP).
“Good clinical practice” (GCP).
Good regulatory practice (GRP).

## Slide 39: GMP Family
Good Distribution Practice (GDP)
Good Transportation Practice (GTP)
Referred to as "GxP" requirements.
Other examples include Good Agriculture Practices, good guidance practices, and good tissue practices.

## Slide 40: Enforcement / Regulatory Agency
In the United Kingdom by the ”Medicines and Healthcare products Regulatory Agency” (MHRA));
in the Republic of Korea (South Korea) by the ”Korea Food & Drug Administration” (KFDA)
in Australia by the “Therapeutical Goods Administration” (TGA)

## Slide 41: Enforcement / Regulatory Agency
in South Africa by the “Medicines Control Council (MCC)”
in Brazil by the ”Agência Nacional de Vigilância Sanitária” (National Health Surveillance Agency Brazil) (ANVISA)
Each of the inspectorates carry out routine GMP inspections to ensure that drug products are produced safely and correctly;

## Slide 42: cGMP
The “current” in current Good Manufacturing Practices allows solutions to technical issues to vary.

## Slide 43: cGMP
Manufacturer can decide individually.
Allows companies to use modern technologies and innovative approaches to achieve higher quality through continual improvement.

## Slide 44: cGMP
Accordingly, the "c" in cGMP stands for "current," requiring companies to use technologies and systems that are up-to-date.
Systems and equipment that may have been "top-of-the-line" to prevent contamination.

## Slide 45: U.S. Food and Drug Administration (FDA)
FDA’s cGMPs regulations provide minimal guidance.
The cGMPs outline facility requirements and the requirements for the documentation of manufacturing procedures.