## Slide 1: BSB3503 - Biomanufacturing CHAPTER 9 Instrument Controls System (Feedback and Feed forward)
Author: Nurul Azyyati Sabri
Co-Author / Editor: Rama Yusvana Faculty Industrial Sciences & Technology yusvana@ump.edu.my

## Slide 2: Learning outcomes
To understand the theory of instruments controls.
To understand the difference between feedback and feed-forward.
To design a feedback control system for component(s) in biomanufacturing.

## Slide 3: “Instrumentation”
"the art and science of measurement and control". en.wikipedia.org/wiki/Instrumentation
Good example: the gauges that control the boilers for the school heating system

## Slide 4: Technical Names
Control
“sequence of decisions aimed at the attainment of specified objectives in an environment of uncertainty and presence of disturbances”.
Control system
“arrangement of physical components connected or related in such a manner as to command, direct, or regulate itself or another system”.
Process control
“Engineering discipline or statistics that deals with architectures, mechanisms, and algorithms for controlling the output of a specific process”.

## Slide 5: Control elements: Sensor
Also called: transducer, probe, gauge, detector, or pick-up
  “Responds to a physical stimulus and transmits a resulting impulse”.

## Slide 6: Type of sensor
Physical sensor
Such as “Length / distance, weight, temperature, pressure, and electricity-for their own sakes”.
Chemical sensor
Specific chemical substance or set of chemicals.

## Slide 7: Type of sensor
Biosensor
Incorporating a biological sensing element.

## Slide 8: “Transducer”
“actuated (or triggered) by power from one system and supplies power (usually in another form) to a second system”.

## Slide 9: “Actuator”
A mechanism for moving or controlling something indirectly instead of by hand.
Hydraulic Actuator uses Oil / Water
Pneumatic Actuator uses air

## Slide 10: Connection of sensors/actuators
The processor should be viewed as a general block
  Microprocessor
  Amplifier
  Driver, etc
Matching: between sensor/processor and processor/actuator

## Slide 11: Example
Sense the temperature of a CPU
Control the speed of the fan to keep the temperature constant
Amplifier
Sensor
Actuator

## Slide 12: “Feed-forward”
Control system which passes a controlling signal from a source to a load elsewhere in its external environment.

## Slide 13: Feed-forward

## Slide 14: “Feed-forward”
Responds to its control signal in a pre-defined way.
Does not observe the output of the processes that it is controlling.

## Slide 15: Feed-forward
Feedforward is an anticipative approach. It does NOT wait until something goes wrong. Feedback is a reactive approach. It responds (reacts) to external environment
Feedforward is unable to respond to disturbances and uncertainties

## Slide 16: Feedback
A process in which a system regulates itself

## Slide 17: Feedback
Such as a heating system
For example,
  uses a thermostat to monitor and adjust its output.

## Slide 18: Feedback
Feedback describes the situation when output influence the same event/phenomenon in the present or future.

## Slide 19: Type of Feedbacks
When feedback acts in response to an event/phenomenon, it can influence the input signal in one of two ways:
Positive feedback
  leading to more modification.
Negative feedback
  Reduce or minimize the error resulting the disturbances

## Slide 20: Feedback
Positive feedback is a self-reinforcing loop.
An event influenced by positive/negative feedbacks can increase or decrease its output/activation until it hits a limiting constraint.

## Slide 21: Feedback
Negative feedback
the feedback signal dampen the effect of the input signal, leading to less modification.

## Slide 22: Ideal feedback model
The feedback is negative if B < 0

## Slide 23: Open-loop Control
A control loop operated by human intervention or does not have a feedback loop to self adjust. http://www.answers.com/topic/open-loop-controller
Example A fan that plugs into the wall with no switch to turn on or off.
Plug fan into outlet power on
Fan operates at the speed of the motor
Unplug fan to shut off
Fan operates to fast to much air movement blows papers of desk

## Slide 24: Closed-loop Control
A control-loop operated by a feedback loop allowing self adjusting of the loop.” A mechanical, optical, or electronic system that is used to maintain a desired output.” http://www.answers.com/topic/control-system
Good example: Fan with a switch to allow the speed to be changed
Fan plugged in
Fan turned on
Fan is to fast papers blow around
Switch turned down to lower fan speed
Fan works fine papers do not blow around
Fan speed can be adjusted or turned off

## Slide 25: Open-loop Controller
An open-loop controller use only the current state and its model of the system.
Does not use feedback to determine if its input has achieved the desired goal.

## Slide 26: Closed-loop controller
The closed loop system has a feedback system to correct errors